## Slide 1: Electron temperature fluctuation measurements with Correlation Electron Cyclotron Emission in L-mode and I-mode plasmas at ASDEX Upgrade
R. Bielajew1, G. D. Conway2, T. Happel2, K. Höfler3,2, P.A. Molina Cabrera2, U. Plank2, P. Rodriguez-Fernandez1, D. Silvagni2, C. Yoo1, A.E. White1, the ASDEX Upgrade Team
1MIT Plasma Science and Fusion Center
2Max Planck Institute for Plasma Physics
3Physics Department E28, Technical University of Munich
This work is supported by the US DOE under Grants DE-SC0006419, DE-FC02-99ER54512- CMOD, and DE- SC0017381. This work has been carried out within the framework of the EUROfusion Consortium and has received funding under grant agreement No 633053. The views and opinions expressed herein do not necessarily reflect those of the European Commission.
21st Joint Workshop on ECE and ECRH
ITER June 20-24, 2022
MIT

## Slide 2: The I-mode improved confinement regime
[Hubbard et al, PoP 2011]
drift
Typically accessed in unfavorable drift configuration ( away from X-point)
Unique I-mode edge features:
Heat transport barrier without particle transport barrier
  Low impurity confinement time
  No ELMs
Separation of transport channels is still under investigation

## Slide 3: Characteristics of pedestal fluctuations across L to I transition on C-Mod and AUG
“Weakly Coherent Mode” (WCM) appears in I-mode and some preceding L-modes
L-mode
I-mode
[Hubbard et al, PoP 2011]
WCM
C-Mod
Reflectometer
Open question: How do changes in fluctuations track changes in transport across the L to I transition?
[Happel et al, Nucl. Mater. Energy 2018]
Reflectometer
CECE
L-mode
I-mode
AUG
“Low Frequency Edge Oscillation” (LFEO) appears in some I-modes
[W. McCarthy, PhD Thesis 2022]

## Slide 4: Several diagnostics at AUG measure edge turbulence
AUG Top View of Port and Diagnostic Access
Correlation Electron Cyclotron Emission radiometers:
  High radial resolution
Toroidally separated CECE: long-range correlation measurements
Reflectometer coupled to CECE: ne-Te cross phase measurements
CECE
CECE
Reflectometer
Experimental design: Discharges with steady-state L-modes and I-modes

## Slide 5: CECE measures presence and coupling of WCM and LFEO in L-mode and I-mode
#39561
3.00-3.95s
#39561
5.10-5.70s
L-mode
I-mode
L-mode
I-mode
AUG CECE
#39561
WCM
LFEO
L-mode
WCM appears in L-mode and I-mode
  Frequency shift correlated with change in
LFEO present in I-mode
LFEO and WCM are coupled in I-mode
WCM-LFEO coupling
No coupling
Cross-bicoherence between neighboring channels
Spectrogram from single CECE channel

## Slide 6: L-mode WCM development in different drift configuration
Time [s]
Radiated power
Core temperature
Core line integrated density
ECRH power (matched)
#40971, 40972
WCM location ()
0.2 MW ECRH
(1.9-2.5s)
Pedestal top ()
0.2 MW ECRH
(1.9-2.5s)
L-mode
0.6 MW ECRH
(2.6-2.9s)
0.6 MW ECRH
(2.6-2.9s)
L-mode
1.8 MW ECRH
(3.7-3.9s)
1.8 MW ECRH
(3.7-3.9s)
Unfav.: L-mode
Fav: H-mode
Matched power discharges in favorable and unfavorable drift configurations
ELM-free H-mode transition

## Slide 7: High resolution CECE provides details of mode radial locations
WCM localized to
Radial extent: 1.5 cm
I-mode
3.0-4.0s
10-250kHz integration
370-400kHz background
#39561
AUG
WCM
WCM peak
LFEO across pedestal
[W. McCarthy, PhD thesis 2022]
Pedestal Top
LCFS

## Slide 8: Long range correlations capture WCM and LFEO
AUG CECE
4.0-5.0s
Toroidal and poloidal separation allow measurement close to same field line with
→ may indicate WCM and LFEO have low n number
LFEO
WCM

## Slide 9: phase diagnostic principles
CECE line of sight
7
9
Reflectometer
(X-mode V-band)
LCFS
6
8
CECE channels
CECE comb and reflectometer cutoff

## Slide 10: phase measurements show slight change between L-mode and I-mode
#39651
CECE-reflectometer
5.1-5.7s
CECE-reflectometer
3.0-4.0s
phase angle measurements from coupled CECE-reflectometer
Coherency between reflectometer and ECE channel at WCM location
Phase angle between fluctuation density and temperature:

## Slide 11: Cross-phase changes with , but WCM cross-phase is more out-of-phase than core broadband turbulence
[Hillesheim et al PoP 2013]
WCM phase more out-of-phase than core turbulence measurements and simulations: characteristic of a different mode?
Cannot directly determine transport from WCM phase
has been shown to change with
AUG edge WCM phase
  L-mode:
  I-mode:

## Slide 12: Summary
CECE comb
  WCM in L-mode and I-mode, more readily in unfavorable drift configuration
  WCM and outer core fluctuation amplitude
  WCM and LFEO localization and coupling
Toroidally separated CECE systems
  WCM and LFEO have low toroidal mode number
phase system
  WCM value: turbulence nature, but limited transport implications
CECE provides detailed investigation of L-mode and I-mode outer core and pedestal fluctuations

## Slide 13: Backups

## Slide 14: Experimental design: discharges with L-mode and I-mode phases
Investigation across parameter space
Density and collisionality: low and high
Heating scheme: NBI and ECRH
I-mode
L-mode
#39561 AUG
Time histories of typical L-mode/I-mode
Notes: ECRH steps from L-mode up to I-mode transition
H1 density: 4.5×10^19 m^(−2)
Pedestal top (𝜌_𝑝𝑜𝑙=0.96) collisionality*
  L-mode 𝜈_𝑒𝑓𝑓=5.6
  I-mode 𝜈_𝑒𝑓𝑓=1.1

## Slide 15: Outer core fluctuations track global confinement
I-mode
3.0-4.0s
10-250kHz integration
370-400kHz background
#39561
AUG
WCM
WCM peak
#38092
AUG CECE
5.1-5.7s
L-mode
#38092
AUG CECE
4.0-5.0s
I-mode
Between L-mode and I-mode, outer core fluctuations:
Decrease by 8% ( to )
Shift to higher frequency

## Slide 16: Phase velocity estimation from slop
#39651
CECE-reflectometer
3.0-4.0s
I-mode
Slope: over 60 kHz
Poloidal separation: mm
  → km/s

## Slide 17: Turbulent electrostatic particle and heat transport
Particle:
Heat:
Electrostatic transport equations
Can the WCM give positive particle and negative heat flux?
: coherency between and
: coherency between and
: coherency between and
: coherency between and
Positive particle flux
Negative heat flux
Positive particle flux and negative heat flux cannot be satisfied in either the near-adiabatic () or far-from-adiabatic () case under these assumptions.
                However,
                phase relations are not straightforward
                and need not be equal
                Electromagnetic transport has contributions from
Assumptions:

## Slide 18: Correlation ECE principles
Correlating neighboring channels gives:
  Frequency spectra
  Fluctuation amplitude
  Correlation length
[S. Freethy EC20 2019]

## Slide 19: Out-of-phase and optical depth
Assumptions:
Reflectivity (???)