## Slide 1: Evaluation of the O-X mode conversion rate of the finite width wave in two dimensional systems
H. IgamiA, A. Fukuyama B, K. Nagasaki C
ANIFS, BGSE, Kyoto Univ., CIAE, Kyoto Univ.
P1
21st JOINT WORKSHOP ON ELECTRON CYCLOTRON EMISSION (ECE) AND ELECTRON CYCLOTRON RESONANCE HEATING (ECRH), 20 - 24 June 2022, ITER Organization

## Slide 2: Contents
Background and Motivation
Configuration of the 2D wave optical calculation with using TASK/WF2D
Calculation results
Summary
P2

## Slide 3: Background and Motivation Mode conversions across the evanescent region
For ECRH in the “over-dense” plasma, the electrostatic EBW should be excited via the mode conversion process from the SX wave at the UHR
Waves launched from the low magnetic field side transmit the evanescent region to couple with the SX-mode
The ray-tracing cannot treat the propagation across the evanescent region
Wave optical full wave analysis is required
SX
?
O
O Evane-scent
EBW
O-SX mode conversion
SX-B mode conversion
∇ne
UHR
X Evane-scent
X Evane-scent
P3

## Slide 4: Broadening of the launched finite width beam affects the O-X mode conversion process
H. Igami. et al.
Plasma and Fusion Research, Volume 11, 2403098(2016)
In 2D configuration, a finite width electromagnetic wave launched from the waveguide at θinj = θopt = arccos(N//opt) is not fully mode converted to the SX mode
At the edge of the launched beam, θinj = θopt ± 1.5 °in this case
P4
In this study, we’ve performed 2D wave optical full wave analyses to provide a guideline for designing the launching beam condition for ECRH by EBW

## Slide 5: Configuration of the 2D calculation
Solving Maxwell equation by finite element method with TASK/WF2D code*)
∇×∇×E – (ω2/c2)ε∙ E=iωμ0 jext
*)A. Fukuyama, et. al 41st European Physical Society Conference on Plasma Physics (EPS 2014) P4.014 (2014)
q
zg
rb
(xbnd, y)
(xbnd, ycnt)
in
wd : Absorber
yd_min
yd_max
x
y
z
=
Gaussian like beam is defined along the y axis at x=xant
P5

## Slide 6: Calculation of the electric field at (xant, yant)
: Cold dielectric tensor
= 0
kin
exd
ezd // B
eyd
2. Solving the Maxwell equations
1. Coordinate transformation
3. Coordinate transformation
P6

## Slide 7: Calculation Parameters
Frequency : f= w/2p = 28GHz
Waist size : = 0.0373m (=3.48l0 )
Mesh size = 0.25mm (~ l0 /40)
thickness of the absorber : wd = 0.025m
Permittivity in the absorber : edamp = e x 2
Normalized collision frequency : ne/w = 0.001, np/w = 0.001, nabs/w = 0.2
Density scale-length at the plasma cutoff,
Ln=7.5* l0 (l0: vacuum wavelength)
Constant magnetic field : |B| = 0.4T, ) wce/w = 0.4
Intel Xeon Silver 4216 CPU @ 2.10GHz, 16C/32T x 2
Memory: 768GB
Number of element : 12096000 (typical)
CPU time : 3196.55 sec (for FEM calculation, typical)
ne/nc = 0.001
P7

## Slide 8: An example of the calculation Launching of the Gaussian like beam with N// = N// opt (q// opt =57.7deg.)
O-mode
Real electric field components
Collisional absorption
Poynting flux
Cold dielectric tensor with weak collisional damping for UH resonant absorption
The artificial dielectric tensor is adopted in FEM calculation inside the artificial “absorption wall ” to make the wave number gradually diverge to cause the resonant absorption like in the UHR
The “absorption wall” has an aperture around the launched wave
wall
electron
P8

## Slide 9: Based on the cold plasma resonant absorption model can be calculated from the outputs of TASK/WF2D
P9
From the collisionally absorbed power
From Poynting fluxes
time average
: O-X mode conversion rate

## Slide 10: Poynting fluxes of various launching angle cases
q = q// opt
q = q// opt -5deg.
q = q// opt -10deg.
q = q// opt +10deg.
q = q// opt +5deg.
=0.15
=0.46
=0.81
=0.46
=0.13
P10
The incident Gaussian like beam is focused on the plasma cutoff for each case

## Slide 11: Calculation results Tox estimated for various propagation angles
Tox is less than plane wave theory at q = q// opt , greater than q ≠ q// opt
P11
TOX = exp{-k0Ln(Y/2)1/2[2(1+Y)(N//-N//opt)2 +Ny2]},
Y = (ce), Nzc ={Y/(1+Y)}-1/2 Mjolhus (1984)
plane wave theory :

## Slide 12: Propagation of waves of a smaller waist size = 0.017m (=1.59l0 )
q = q// opt
q = q// opt -5deg.
q = q// opt -10deg.
q = q// opt +10deg.
q = q// opt +5deg.
=0.226
=0.454
=0.576
=0.471
=0.267
q = q// opt : decreases
q = q// opt ±10 deg. : increases
P12

## Slide 13: Tox estimated for various beam waist sizes for various propagation angles
With increase of the beam waist size w0, numerically calculated Tox with taking N//=N//opt, approaches 1
P13

## Slide 14: The effect of the beam curvature radius Rc on the Tox is investigated with changing the beam focal point
P14
TOX remains to be constant for the same beam waist size w0 since the N// Fourier spectrum is conserved in the slab plasma in the uniform magnetic field.
With introducing the magnetic shear, TOX can change because the N// spectrum can change during the wave propagation
, x=x_PC

## Slide 15: Ln=7.5* l0 , w0 /l0 =1.59
P15
zPC/l0 =0
zPC/l0 =30
zPC/l0 =-30
zPC/l0 =20
zPC/l0 =-20
The phase and amplitude along the y-axis vary with the propagation
On the other hand, the N// Fourier spectrum is conserved
zPC : Distance between the beam focal point ant the plasma cutoff

## Slide 16: Ln=7.5* l0 , w0 /l0 =5.006
P16
zPC/l0 =0
zPC/l0 = 100.0
zPC/l0 =-100.0
zPC/l0 =50.0
zPC/l0 =-30.0
With adopting a larger beam waist size w0, the spreading of the N// Fourier spectrum can be reduced to obtain higher TOX

## Slide 17: Tox with change of the beam waist size w0 for the case of wce/w = 0.4 and 0.8
w0/l0 > 6 is required for Tox > 90 % with Ln/l0 =7.5
Higher Tox can be obtained with lower wce/w for the small waist size beam
P17

## Slide 18: Estimation of Tox with change of the density gradient
Tox decreases as increase of Ln, however, it converges with 80% for Ln/l0 > 30
P18
H. Igami et al., Plasma Phys. Control. Fusion 48 (2006) 573–598
Decrement of Tox in low Ln/l0 region might cause by transmission of the X-mode toward the lower density side after the O-X mode conversion as the 1D calculation suggested

## Slide 19: Summary : purpose and method
To provide a guideline for designing the launching beam for ECRH by EBW, wave optical analyses were performed for various normalized density scale lengths and beam parameters with using of TASK/WF2D code
TOX is estimated based on the cold plasma UH resonant absorption model in slab plasmas in the uniform magnetic field
P19

## Slide 20: Summary : results and future works
The beam waist size w0 affects Tox
With adopting sufficiently large w0/l0, higher TOX can be obtained so that the spreading of the N// Fourier spectrum can be reduced
  consistent with the previous 2D numerical analysis (Y. Oka, et al., COMSOL Conference 2020, K. Nagasaki et al., EPS 2020)
Though Tox decreases as increase of Ln, it converges with 80 % for Ln/l0 > 30 with adopting sufficiently large w0/l0 (≳ 5 )
Future works
Effect of the magnetic shear on for finite width waves
Propagation characteristics during the X-B mode with introducing integral from of dielectric tensor
P20