## Slide 1: Experiments with reduced single pass absorption at ASDEX Upgrade - instrumentation and applications Martin Schubert, J. Stober, A. Herrmann, E. Grigore 1, W. Kasparek 2, C. Lechte 2, F. Monaco, B. Petzold, B. Plaum 2, E. Poli, C. Ruset 1, S. Vorbrugg, D. Wagner, ASDEX Upgrade Team 3
Max-Planck-Institut für Plasmaphysik, Garching
1 Institute for Laser, Plasma and Radiation Physics, Magurele, Romania
2 Institut für Grenzflächenverfahrenstechnik und Plasmatechnologie, Stuttgart
3 See author list of U. Stroth et al. 2022 Nucl. Fusion 62 042006

## Slide 2: Contents
Two-pass scheme ASDEX Upgrade
Thermocouple measurement within the reflecting gratings
Data evaluation
Exemplary results
Summary

## Slide 3: Two-pass scheme ASDEX Upgrade
Top view ASDEX Upgrade (AUG) with segment numbers
Eight ECRH launchers in Segments:
5 (x4), 6, 8, 14 (x2)
Launchers Seg 5 stacked vertically
Reflected beams Seg 5 on top of incoming
Heat Shield: position on the inner column of AUG, where reflecting gratings are mounted
Design of oblique geometry in order to maximize O-2 absorption

## Slide 4: Inside the AUG vacuum vessel: ECRH Launchers
Robust surfaces and auxiliary limiters were used as designed end point after 2nd pass
This launcher #6 will be used later

## Slide 5: Inside AUG vac vessel: Heat Shield, reflecting gratings
Seg 4
Seg 5
Seg 6
Seg 7
Seg 13
Seg 13

## Slide 6: Tungsten coating of W1.4901 steel
Gratings in Seg7 and Seg13 manufactured out of W1.4901 steel
Coating necessary to increase reflectivity
Thin tungsten coating ~ 10 µm using Mo interlayer
Technique newly developed by INFLPR, Magurele, Romania

## Slide 7: Thermocouple measurement, reflecting gratings
Idea: flush-mounted thermocouple
Borehole diameter 0.5 mm
Thermocouple, outer diameter 250 µm Type K, NiCr-Ni, Tmax 1300 ºC sensitivity 40.96 µV / K
Side view of the tile
cable
Plasma facing side
Incoming mm-wave power
Roessel Messtechnik GmbH, PI 071 Mantel-Thermoelemente

## Slide 8: Thermocouple mount - assembly
Ensure flush-mount
Optimized design: cable channels built-in into the tile
Additional cable shielding by flexible metal tube
Acknowledgement: H. Schütz for careful mechanical work

## Slide 9: Thermocouple mount - finish
Microscope photo

## Slide 10: Data evaluation
Power
ΔT
t
ΔT
t
Large bulk, temperature sensor inside the bulk
What is the consequence of the flush mount?
Timing of pulse train comparable to characteristic time of the sensor

## Slide 11: Signal and background – AUG #39747, Gyrotron #6
Timing of Gyrotron 6, model amplitude
Thermocouple signal compared to averaged background (red)
Last row: distant thermocouples, not hit by mm-wave beam, artificial offset for better visibility
  No trace of mm-wave pulse train on distant thermocouples
  Background (plasma load) can be assumed homogeneous across tile
ΔT
~ 10 ms
ΔT
Signal temperature after one pulse train does not return to the background level
Characteristic time delay ο(10 ms) of the temperature signal

## Slide 12: Evaluation model
CSM TSM = ASM (pbg + pA) – kSM (TSM – TM)
CM TM = kSM (TSM – TM) – kMN (TM – TNB)
fNB CB TNB = fNB Atl (pbg + pA) + kMN (TM – TNB) – kNB (TNB – TIB)
fIB CB TIB = fIB Atl (pbg + rIB · pA)
ASM
CSM
CM
kSM
kMN
TNB
“Near Bulk”
Atl
CB (entire tile)
ASM
fIB Atl
ANB = fNB Atl
For simplicity: set next temperature zone TIB as boundary condition, no energy flow from TNB
Apply fraction rIB of Gyrotron power, important for the baseline in the measurement signal
·
·
·
·
TM measured quantity
pA absorbed mm-wave intensity
pbg (homogeneous) background intensity
“intermediate bulk”

## Slide 13: Exemplary results – setup 1/3
Fast steerable launchers
Push-rod position

## Slide 14: Exemplary results – setup 2/3
Timing of Gyrotron pulses and push-rod position

## Slide 15: Exemplary results – setup 3/3
126 mm
44 mm
Heat shield, reflecting grating (double tile)
Beam position on the Heat Shield for the five pulses in the pulse train, function of the push-rod position

## Slide 16: Calibration in empty vessel – AUG #39744
Fit converges, all parameters seem well defined, e.g. CSM/kSM = 30 ms kSM/ASM = 15000 W / (K m2) = λ/d λ specific heat conductivity λ ~ 1 W /(K m), d ~ 10-4 m
Additional signal delay with respect to the Gyrotron power signal improves the fit (approx. 1 ms)
Fit parameter values seem to be reasonably consistent with Thermocouple specifications and material properties
Residual can be explained by change of real pA during pulse (launcher/beam movement)
Measurement
Model
TNB
TIB

## Slide 17: Experiment on X-3 absorption AUG #39747 - overview

## Slide 18: Experiment on X-3 absorption AUG #39747 – geometry
Heating 105 GHz
Probing 140 GHz
See also:
talk by
J. Stober

## Slide 19: Experiment on X-3 absorption AUG #39747 – model result
Measurement
Model
TNB
TIB
Using fitted material constants from the vacuum measurement
Fit parameter rIB must be free (baseline)
Main result (pulse train amplitudes) seems robust.
rIB seems to vary: Dynamic misalignment? Change of beam width?
Fitted power data used for the results in the talk by J. Stober

## Slide 20: Monitoring O-2 shine-through
Beam of Elisey 3M, O-2 polarisation, 20-40 ms pulses data points taken 2017 and 2019 in „Std H mode“ type plasma experiments
Pulse response of one Thermocouple (R8) on shine through power 2D function of launcher setting
a [mm]
ß [deg]
approx. 5 cm on Heat Shield
a [mm]
ß [deg]
push-rod pos.
toroidal rot.

## Slide 21: Summary
Development of measuring tools to study mm-wave deposited power on the heat shield of AUG with high time resolution
Modelling tools may help to understand details of the heat flow, can be used for planning and preparation
Possible application may also be monitoring of beam geometry and size, systematic comparison with beam tracing prediction seems possible