## Slide 1: Triple-Beampath-scenario for O2-heating at Wendelstein 7-X: experience of OP1.2 and final improvements for OP2
T. Stange, K.-J. Brunner, U. Höfel, H. P. Laqua, C. Lechte, S. Marsen, D. Moseev, B. Plaum, T. Bräuer, C. P. Dhard, M. Endler, E. Grigore, N. Marushchenko, D. Naujoks, Y. Turkin, F. Warner, R. Wolf and the W7-X team

## Slide 2: Motivation and Outline
Motivation
  The stellarator Wendelstein 7-X (W7-X) operating @ 2.5 T has the final goal to demonstrate 30 min operation at reactor relevant parameters (Te,i > 3 keV @ ne > 1020 m-3)
  only ECRH steady state capable (2nd harmonic heating @ 140 GHz)
  steady state O2-heating scenario necessary to allow ne > nX2-cutoff = 1.2 ∙ 1020 m-3
Outline
  Reminder: Setup of the ECRH system
  Design of O2-scenario
  Experimental results of OP1.2
  Optimization of O2-scenario for OP2
  Summary + Outlook
Island divertor

## Slide 3: 1. Reminder: Setup of the ECRH system – top view
Fully quasioptical transmission line in air (first of its kind!)
Gyrotrons in two rows for module 1 and 5
A1
B1
C1
D1
E1
A5
B5
C5
D5
E5
F5
Coupling to plasma by 4 equatorial front steering launchers
with 3 Front steering mirrors each
Vacuum valve with diamond window
2D-front
steering mirrors
  biggest ECRH facility in the world (10 MW-class gyrotrons @ 140GHz)
  Injected power: 7.5 MW (up to now)
=> See talk by H. P. Laqua: ECRH-Power Upgrade at W7-X (Tuesday 17:00)
5
1
2
3
4

## Slide 4: 2. Design of O2-scenario: Holographic gratings @ ASDEX Upgrade
single pass absorption < 80 % even with central Te ≥ 3 keV
Incidence angle > 11°
Use of reflector tiles at high field side wall to allow directed 2nd pass
Incident beam with incomplete absorption
Natural reflection of first wall
Optimized reflection
Example W7-X @ central values: Te=3keV, ne=1020 m-3
Development of holographic gratings for ASDEX upgrade by IGVP Stuttgart:
holographic grating to allow diﬀering angles of incidence and reflection (3D for refocusing)
Reflected beam close to incident beam
Optimization for no phase shift between TE and TM (reflector acts as plane reflector with regard to polarization)
double-path-absorption: up to 90 %
[IGVP]
Top view
Axis
B
Graphite tile for AUG produced @ IGVP workshop

## Slide 5: 2. Design of O2-scenario: Conditions for O2 @ W7-X
  Different situation of first wall in W7-X
  Usual size of graphite tiles < 3w
  graphite tiles with up to 5% absorption would heat up to > 1000°C (400°C limit for CuCrZr)
  replacement by molebdenum alloy (TZM) - good electrical + thermal conductivity - easy to manufacture
  heat load < 1 kW with 0.3% absorption
  possibility to use advanced mounting to allow undisturbed reflector surface
stainless steel panels at low field side
Graphite tiles opposite to ECRH launchers
ECRH launchers
CuCrZ-heatsinks brazed on stainless steel cooling pipes
[IPP, Foto: Volker Steger]

## Slide 6: 2. Design of O2-scenario: Triple-beampath @ W7-X in OP1.2
  Further improvement at W7-X: third beampath by reflection at wide polished steel panel
  Refocussing + decreasing of stray radiation by factor 2
  Design conditions for OP1.2
  1st + 2nd pass through plasma axis
  Maximize central Te + absorption
  moderate incidence angles < 15°
  2nd pass safely hit steel panel & 3rd pass close to plasma axis
  Do not care that much about polarization losses
Graphite tiles opposite to ECRH launchers
Polished stainless steel panel
[IPP, Foto: Volker Steger]

## Slide 7: 2. Design of O2-scenario: Expected efficiency in OP1.2
OP1.2: Holographic grating (by IGVP Stuttgart) to allow on axis in 1st + 2nd pass
Comparative TRAVIS-calculations:
flat ne- and peaked Te-profile Te = 3 keV ne = 1.2 ∙1020 m-3
2 of 5 tiles with flat surface only
holographic grating + plane surfaces w/o polarization matching → 40% of shinethrough converted into X-mode
Polished stainless
steel panel
p1st pass = 73 % p2nd pass = 50 % p3rd pass = 48 % pshine = 1 %
pstray = 11..13 %
Example: Charly 1-beamline
B1
A1
D1
E1
C1
Beam- line | Pstray after 3 passes OP1.2
A1 | 21 %
B1 | 14 %
C1 | 11 %
D1 | 14 %
E1 | 12 %
Average | 14 %

## Slide 8: 3. OP1.2 results: X2-operation
X2-operation with absorption ≈ 100 % & quite high Te up to 10 keV, but flat density profiles in gas fueled discharges with Ti < 1.5 keV
Clamping of Ti by enhanced core turbulence (TEM/ITG)
Peaked Ti-profiles only demonstrated with peaked ne-profiles
[M.N.A. Beurskens et al 2021 Nucl. Fusion 61 116072]
[S.A. Bozhenkov et al 2020 Nucl. Fusion 60 066011]
[J A Alcusón et al 2020 Plasma Phys. Control. Fusion 62 035005]
stability valley
Envisaged density range

## Slide 9: 3. OP1.2 results: O2 beyond X2-cutoff with pellets
X2-startup + dynamic change to O2 in the first 2s
Pellets to steepen density profile & overcome X2-cutoff
Low stray radiation demonstrated @ envisaged optimal Te = 3 keV (after restart of startup gyrotrons)
Demonstration of efficient power transfer of Te to Ti in an electron heated high density scenario
TRAVIS results in very good agreement with measurements
20171115.039

## Slide 10: 3. OP1.2 results: O2 beyond X2-cutoff with gaspuff
ne
Te
LCFS
Total power of 9 gyrotrons (dynamic change from X2-startup to O2-polarization within first 2s)
Te by ECE @141GHz in cutoff
Te by Thomson
Line integrated density
ECRH stray radiation
Plasma energy
Ti by XICS
Feedback
gas flux [mbar∙l/s]
0
0 2 4 6 8 10 12 14
2.5 keV to 1.5 keV lead to factor 4 in stray radiation!
repeat operation beyond X2-cutoff by gas puffing only
steady state beyond X2-cutoff + intrinsically achieving or almost close to detachment (no power load on divertors)
slightly peaked ne-profile!
eventually promising scenario to overcome clamping limit, but low Te did not allow to prove high performance
Power upgrade + optimization of O2-scenario
Ti
[H. P. Laqua, … T. Stange, … et al 2021 Nucl. Fusion 61 106005]
20180904.015

## Slide 11: 4. Optimization of O2-scenario: Deposition profile
Separation of Ti and Te supported by to high power deposition density
Neoclassical transport simulations (NTSS): no change of performance with regard to Ti for deposition reff/a < 0.3
Design conditions for OP2
Allow slight off axis beampaths to use natural shape of inner wall
in this sense favor use of polarization over holographic gratings (which have in general polarization loss + lower efficiency)
in case of holographic gratings allow only 2nd pass close to 1st pass
Use already polished panel as reflector for 3rd pass
favor scenarios with higher 1st pass absorption
allow incidence angles < 20°
NTSS-calculation including 1/n turbulent transport with χ = 0.5 m2/s @ reﬀ = a

## Slide 12: 4. Optimization of O2-scenario: triple-beampath OP1.2 vs OP2
Residual stray radiation mostly
in shinethrough after 3rd pass
full polarization matching
OP1.2: Holographic grating (by IGVP Stuttgart) to allow on axis in 1st + 2nd pass
OP2: Slightly off-axis + polarization grating to allow pure O-mode in 2nd pass
Further absorption in 4th pass BUT: tungsten coating of
graphite tiles necessary
to do not overheat!!!
reduction of stray radiation by factor 2
High mode purity & beam focusing allows redirection into 4th path
TZM-tile with holographic grating but without polarization matching → 40% of shinethrough converted into X-mode
Polished stainless
steel panel
p1st pass = 73 % p2nd pass = 50 % p3rd pass = 48 % pshine = 1 %
pstray = 11..13 %
p1st pass = 68 % p2nd pass = 63 %
p3rd pass = 46 % pshine = 5 %
pstray = 6..8 %
Example: Charly 1-beamline

## Slide 13: 4. Optimization of O2-scenario: polarization gratings
OP2
E1
D1
C1
B1
B1
A1
D1
E1
C1
OP1.2
Flat reflectors with polarization gratings for 4 of 5 former beams of OP1.2
tile surface increased as much as possible + field line shadow by surrounding tiles
Sinusoidal gratings produced by wire erosion (< 0.5 k€/tile)

## Slide 14: 4. Optimization of O2-scenario: polarization gratings
OP2
E1
D1
C1
B1
grating orientation (mostly) parallel to field lines at inner wall
no leading edge + low O-mode loss (but maximum X-mode loss)
polarization correction works for both B-field directions+both modes
Optimum with regard to depth & acceptance angle but works only for B+
Reflected O-mode part for B-
Except E1 + E5 with roof-edge surface
Final params: deff = 0.565mm dreal = 0.84mm
Flexible solution
Reflected O-mode part for B+

## Slide 15: 4. Optimization of O2-scenario: holographic reflectors for A+F
OP2
E1
D1
C1
B1
„Virtual“ reflector tiles of F-beamline
Old holographic A1-tile not used anymore because steering range of A1 (& F1) to the right is too small
tiles in opposite direction are used with holographic grating to reflect the beam back to the stainless panel
Beam broadening in vertical direction
use of 3 tiles
Old A1 tile
C1
D1
E1
B1
New A1
Backside view on reflector tile with polarization gratings

## Slide 16: 4. Optimization of O2-scenario: segmented holographic reflectors
[B. Plaum, IGVP Stuttgart]
TE
TM
[C. Lechte, IGVP Stuttgart]
Holographic grating distributed @ up to 3 tiles
redesign of first wall tiles with as-built- geometry of CuCrZr-structure to achieve necessary accuracy of combined reflectors
3D-holographic gratings calculated for each individual surface
final efficiency by full wave simulations
TE and TM of ideal grating with almost equal efficiency of up to 90%
gratings separately milled into TZM-tiles by special technique at workshop of IGVP Stuttgart
TZM
Graphite

## Slide 17: 4. Optimization of O2-scenario: proof of beam accuracy
Horn antenna with up to 10W
Matching mirror
Tiles with combined grating
Ecosorb screen
Simulate expected beam shape during plasma operation
Good agreement with Expected position and beam shape
Variations on the grating without obvious problems
Expected position
Envisaged position of incident beam

## Slide 18: 4. Optimization of O2-scenario: practical issues
Mounting of holographic reflectors:
accurate positioning to each other & in relation to CuCrZr-structure by 3D-printed support structure of plastic
Safety issues:
W-coating of surrounding graphite tiles
dots (Ø 4mm) around reflector tiles without W-coating for IR-observation
Identification if beam leaves the tile

## Slide 19: 4. Optimization of O2-scenario: Hardening of heatshield
Tungsten coating of almost whole ECRH-heatshield in module 1 and 5
Heatshield module 1
Tungsten coated graphite tiles
Tungsten coated TZM tiles for O2
Area affected by stray radiation after 3rd pass
X2-positions

## Slide 20: 4. Optimization of O2-scenario: Expected efficiency OP1.2 vs OP2
O2-heating B‘axis,0° = 2.57T ne,0 = 12 ∙1019 m-3
Overview of improvement of stray radiation after 3 beam passes
For information: Shinethrough after 2nd and 3rd pass for OP2-config
Beamline | Pstray after 3 passes OP1.2 | Pstray after 3 passes OP2 | Pshine after 2nd pass OP2 | Pshine after 3rd pass OP2
A1 | 21 % | 10 % | 9 % | 2 %
B1 | 14 % | 7 % | 14 % | 5 %
C1 | 11 % | 6 % | 12 % | 5 %
D1 | 14 % | 6 % | 10 % | 3 %
E1 | 12 % | 5 % | 8 % | 2 %
F1 | - | 8 % | 6 % | 2 %
Average | 14 % | 7 % | 10 % | 3 %
reduction of stray radiation by factor 2
High mode purity & beam focusing allows redirection into 4th pass
Power deposition of Modul 1 beams

## Slide 21: Summary and Outlook
Main results of OP1.2
  successful implementation of a triple-beampath scenario for O2-operation
  first demonstration of reactor relevant plasmas sustained by O2-ECRH only
  measured absorption in very good agreement with theory
  Improvements for OP2:
  polarization matching of 2nd pass for all beams which mainly determines overall efficiency
  Reduction of stray radiation by factor 2 due to advanced use of holographic + polarization gratings
  tungsten coating of complete inner heatshield to allow 4th pass
Outlook
  further flat reflectors with polarization gratings for high density X3-operation
  broad polarization gratings on stainless steel panel to allow matched 3rd pass
  eventually further O2-tiles to allow finite current drive in O2-scenarios
Te = 3 keV

## Slide 22: Thank you for attention
[IPP, Foto: Jan Hosan]