## Slide 1
Lynda Boukela (DESY)
AI AND LARGE DATA VISUALIZATION WORKSHOP
Princeton University, 13th June 2024
Enhanced Quench Detection at the EuXFEL
Through a Machine Learning-Powered Approach

## Slide 2: Agenda
01 The EuXFEL
In general
Operational overview
The SRFCs
02 Quench detection
Current solution
Model-based fault detection
ML-based quench identification
03 Deployment and evaluation
Data acquisition, postmortem analysis
Evaluation, station-wise and pulse-wise
Reports
Data labeling
04 Outlook

## Slide 3: The EuXFEL

## Slide 4: The EuXFEL
In general
Light to probe matter
The European X-Ray Free Electron Laser (EuXFEL), largest particle accelerator for X-ray laser generation worldwide
Up to 17 GeV, 27000 extremely intense laser ﬂashes per second
Located in Hamburg, Germany
Total length of 3.4 kilometers
Several hundred users every year, the availability of the facility is crucial
The course of the European XFEL
  © DESY / R. Schaaf und D. Schröder

## Slide 5: The EuXFEL
Operational overview

## Slide 6: The EuXFEL
Operational overview
  © DESY 2017
25 stations

## Slide 7: The EuXFEL
The SRFCs
  © DESY 2017
25 stations
32 SRFCs
,
  Resonators (1.3GHz)
  Controlled and monitored with the LLRF system
  Average accelerating field of 23.6 MV/m
  Operated in a pulsed mode, repetition rate of 10 Hz, duration 1.8 ms

## Slide 8: Quench detection

## Slide 9: Quench detection
Current solution
Detection through the QL-based quench QDS
Running average from previous 100 pulses
The QDS triggers an alarm if the QL computed for a single pulse drops below the running average by more than a user-defined threshold (typically 10% of the nominal QL value)
This approach, however, suffers from robustness issues
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
Branlard J. et. al. Superconducting cavity quench detection and prevention for the European XFEL. ICALEPCS (2013)
  - External: power dissipation induced by the coupling process
  - Unloaded: power dissipation through the cavity walls
Loaded
External
Unloaded
Notes: Ql=wW/Pdiss >> Energy/Power
The unloaded quality factor lies at Q0 ~ 2x 10^10, while the
external quality factor is in a range of 10^6 < Qext < 10^8.

## Slide 10: Quench detection
Model-based fault detection
  © DESY / R. Schaaf und D. Schröder
: Half bandwidth
: Detuning
: Beam field
Electromagnetic dynamics
,
Schilcher, T. Vector sum control of pulsed accelerating fields in Lorentz force detuned superconducting cavities. Ph.D. thesis, University of Hamburg. (1998)

## Slide 11: Quench detection
Model-based fault detection
  © DESY / R. Schaaf und D. Schröder
,
Residuals (parity space)
Statistical test (GLR)
Eichler A. et. al. Anomaly detection at the European X-ray free electron laser using
a parity-space-based method. Phys. Rev. Accel. Beams (2023)

## Slide 12: Quench detection
Model-based fault detection
  © DESY / R. Schaaf und D. Schröder
Quench
Other faulty behavior

## Slide 13: Quench detection
ML-based quench identification
  © DESY 2017
  © DESY 2017
  © DESY 2017
K-medoids to build a profile of the quenches
Two models based on two similarity measures (EUC and DTW)
The traces are normalized and / or reduced
In the example, DTW=2.8 and EUC=18.6

## Slide 14: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
With both models, two clusters and medoids are obtained
Data from 2021 are used, 76 quenching traces
Assignment mainly with respect to time of occurrence of the quenches

## Slide 15: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference in distance space
Fitting different based on the similarity measure
Thresholds & decision boundaries

## Slide 16: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference in distance space
Fitting different based on the similarity measure
Thresholds & decision boundaries
EUC

## Slide 17: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference in distance space
Fitting different based on the similarity measure
Thresholds & decision boundaries
DTW

## Slide 18: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
Inference in distance space
MLP
Three hidden layers
Imbalanced data
Based on EUC
1st value: TPR
2nd value: FPR
3rd value: ROC-AUC

## Slide 19: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference in distance space
MLP
Three hidden layers
Imbalanced data
Based on DTW
1st value: TPR
2nd value: FPR
3rd value: ROC-AUC

## Slide 20: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
Inference based on the GLR
CNN
Three hidden layers
Max normalization
Imbalanced data
1st value: TPR
2nd value: FPR
3rd value: ROC-AUC

## Slide 21: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference based on the GLR
AE-based quench profile
Two layers in each part
Max normalization
Mean absolute error or mean squared error for the reconstruction
1st value: TPR
2nd value: FPR
3rd value: ROC-AUC
MAE

## Slide 22: Quench detection
ML-based quench identification
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Inference based on the RF
CNN
Three hidden layers
Based on the three signals
Imbalanced data
MAE
1st value: TPR
2nd value: FPR
3rd value: ROC-AUC

## Slide 23: Deployment & Evaluation

## Slide 24: Deployment & Evaluation
Data acquisition, postmortem analysis
Notes: 1.5 GB/s data from RF field measurements

## Slide 25: Deployment & Evaluation
Data acquisition, postmortem analysis
Timm, J., et al. The trip event logger for online fault diagnosis at the European XFEL.IPAC, (2021)
  250 pulses (50 first nominal)
  RF signals sampled at 1 Mhz (1820 samples)
  Saved into files, corresponding to station events

## Slide 26: Deployment & Evaluation
Evaluation, station-wise
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Data collected from January to December 2022
  671 events, 354 were detected as faults within the SRFCs, 87 corresponding to quenches
Evaluation and comparison based on the station events, using the TPR, the FPR and the ROC-AUC
A clear improvement of the quench identification compared to the QDS
  QDS : TPR = 0.93 and FPR = 0.20
  EUC : TPR = 0.95 and FPR = 0.07
  DTW : TPR = 0.93 and FPR = 0.04
TP : the method accurately identified a quench
TN : the method accurately recognized a fault was not a quench
FP : the method identified a quench that’s in reality not a quench
FN : the algorithm failed to identify a real quench

## Slide 27: Deployment & Evaluation
Evaluation, pulse-wise
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
ROC-AUC=99.3
FPR=0.06
TPR=98.6
(euc)

## Slide 28: Deployment & Evaluation
Reports
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Affected stations
Number of affected cavities
Number of faulty pulses
Number of quenching pulses
Number of missing signals
Ignored cavity
Reports are generated to gain insights
Emails, Web interface
Daily reports

## Slide 29: Deployment & Evaluation
Reports
  © DESY / R. Schaaf und D. Schröder
  © DESY 2017
  © DESY 2017
  © DESY 2017
Reports are generated to gain insights
Emails, Web interface
Details on the known faulty pulses
RF signals, residuals and GLR of the known faulty pulses
Daily reports

## Slide 30: Deployment & Evaluation
Reports
  © DESY / R. Schaaf und D. Schröder
Reports are generated to gain insights
Emails, Web interface
Yearly / half-yearly reports
Distribution of the faults and quenches over the year 2022
Distribution of the quenches over the stations and the cavities in 2022

## Slide 31: Deployment & Evaluation
Data labeling
  © DESY / R. Schaaf und D. Schröder
Help from the LLRF experts with the data labeling
Difficult and time-consuming task, thousands of traces
A GUI and a web application are being developed
Help in the process through the QDS findings with the station events, and the ML predictions with the pulses

## Slide 32: Outlook

## Slide 33: Outlook
Results validation, more data, but smarter labeling ( with an expert-in-the-loop strategy)
Explore other neural network architectures for the quench detection
Go online, firmware implementation has already been initiated
Explore the possibility of early detection
Incremental learning to scale up and detect more anomalies

## Slide 34
Lynda Boukela
MSK
lynda.boukela@desy.de