## Slide 1
Chats 2021 - via remote video system
Parametric study and optimization of
the cryo-magnetic system
for EU DEMO at the pre-conceptual design phase
CEA/DRF/IRIG: Christine Hoa, François Bonne, Thomas Latella
CEA/DRF/IRFM: Quentin Le Coz, Louis Zani, Benoît Lacroix
West Pomeranian University of Technology: Monika Lewandowska
EPFL/SPC: Kamil Sedlak
ENEA: Valentina Corato
Notes: 15 mn (12mn +3mn)

## Slide 2: Contents
Introduction and context
Parametric study and optimization methodology
Thermal-hydraulic description and assumptions
Comparative results
Conclusions and perspectives

## Slide 3: Introduction - Context
Pre-conceptual design of EU DEMO magnets, include eletromagnetic, mechanical, thermal-hydraulic and also cryogenic studies
Toroidal Field superconducting magnets
  3 cable-in-conduit conductor designs (2015)
    ITER-like: double pancake design
    Graded conductors: layer design
  Objective: to find cost effective solutions for the superconducting magnets and their cooling systems

## Slide 4: Introduction – Context
Parameters | ITER | DEMO
Plasma major radius (m) | 6.2 | 9.1
Plasma current Ip (MA) | 15 | 20
Plasma volume (m3) | 830 | 2500
Toroidal field BT (T) | 5.3 | 5.7
Pulse length | 400 s | >2 h
Magnet system total weight (ton) | 10135 | 17000
Equivalent refrigeration power at 4,5 K | 3*25 kW (40-110 kW) | To be optimized at the conceptual design phase
Cryo-distribution | 4 loops (2000-2700 g/s) Tin=4,5 K =[0,5-1,1] bar Cryomachines 10 kW (30% refrigeration loads) | 
Parameters | ITER | DEMO
Plasma major radius (m) | 6.2 | 9.1
Plasma current Ip (MA) | 15 | 20
Plasma volume (m3) | 830 | 2500
Toroidal field BT (T) | 5.3 | 5.7
Pulse length | 400 s | >2 h
Magnet system total weight (ton) | 10135 | 17000
Equivalent refrigeration power at 4,5 K | 3*25 kW (40-110 kW) | To be optimized at the conceptual design phase
Cryo-distribution |  | 

## Slide 5: Introduction – Thermal-hydraulics
Introduction
Supercritical helium at
Tin= 4.5 K, Pin=6 bar,
= 1 bar
(reference case)
Temperature margin w.r.t to current sharing temperature
(Tcs (x)- Tcicc (x) ) > 1,5 K
What is the optimized (magnet+ cryogenic distribution)?
Parametric studies Tin and
Plasma
Nuclear heating,
AC losses, radiation,
conduction,
joints….

## Slide 6: Conductor design options
Double pancake
Double layers
single layer

## Slide 7: Parametric studies and optimization methodology
SIMCRYOGENICS
1D CICC model
Inter-turn /Inter layer coupling
Parametric studies
TF coil with a CICC design
SIMCRYOGENICS
Optimization algorithm
(Cryodistribution SHe loop+ CICC model
Nuclear heating
Cross-checks
TACTICS: THEA/CAST3M model
Inter-turn coupling
Analytical model
1D CICC model
no inter-turn coupling
Parametric studies
  Variable Parameters
      Tinlet = [4.0- 4.6] K
      ΔP= [0.2-1.2] bar

## Slide 8: Thermal-hydraulics description

## Slide 9: Simcryogenics modelling

## Slide 10: Optimization parameters
WP1 and WP2:
WP3:
For WP1 and WP2:
For WP3:
Prefr, reference(W) with Tin= 4.5 K, Pin=6 bar, = 1 bar
(ITER-like)
Prefr, reference(W) reference refrigeration power
Prefr, optimized (W)
  Refrigeration power layer by layer adapted for a graded cooling system, with different supply temperatures and mass flows
  Global refrigeration power for 1 TF with parallel distribution, one temperature supply
    Layer design: non homogeneous mass flow distribution
    Pancake design: homogeneous mass flow distribution
ideal refrigeration power at 300 K with respect to Carnot factor

## Slide 11: Comparative results – layer by layer
Layers | L1 | L2 | L3 | L4 | L5 | L6 | L7 | L8 | L9 | L10 | L11 | L12
∆P (bar) | 0,30 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25 | 0,25
Tinlet (K) | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5 | 4,5
Prefr, reference (W) | 59 | 50 | 44 | 37 | 33 | 27 | 23 | 19 | 16 | 13 | 11 | 9
Prefr, optimizedW) | 42 | 33 | 27 | 23 | 19 | 16 | 13 | 11 | 8 | 7 | 7 | 5
Power saving (%) | -29 | -34 | -39 | -39 | -43 | -43 | -44 | -44 | -46 | -45 | -39 | -49
Heat loads (W) | 38,1 | 30,1 | 24,4 | 20,3 | 16,7 | 13,8 | 11,2 | 9,2 | 7,2 | 6,2 | 5,3 | 3,7
Each layer is optimized independently
One optimized temperature: 4.5 K
Optimized ∆P : 0,3 bar and 0,25 bar
Power saving with respect to reference case (4.5 K, 1 bar) from 30% to 50%
WP#1 (SPC design) : 12 layers

## Slide 12: Comparative results – layer by layer
Double layers | DL1 | DL2 | DL3 | DL4 | DL5 | DL6
∆P (bar) | 1,20 | 1,20 | 0,53 | 0,32 | 0,36 | 0,25
Tinlet (K) | 4,3 | 4,4 | 4,5 | 4,5 | 4,2 | 4,5
Prefr, reference(W) | 80 | 51 | 34 | 22 | 16 | 13
Prefr, optimizedW) | 89 | 56 | 29 | 17 | 12 | 6
Power saving (%) | +12 | +9 | -14 | -26 | -24 | -57
Heat loads (W) | 70 | 42 | 26 | 15 | 9 | 5
Each double layer is optimized independently
Large range optimized temperatures: 4.2 K to 4.5 K
Large range of optimized ∆P : 0.32 to 1.2 bar
With the reference cooling parameters (4.5 K, 1 bar), DL1 and DL2 are not compliant with the temperature margin of 1.5 K
Double layer design would benefit from a graded cooling scheme

## Slide 13: Comparative results- global optimization WP1
∆P (bar) | 0,48
Tinlet (K) | 4,6
Prefr, reference(W) | 342
Prefr, optimized(W) | 229
Power saving (%) | -33
Heat loads (W) | 186
Inter-turn and inter-layer impact the heat load distribution
Layer L11 is the most critical one: the Tmargin=1,5 K is located at the end of the conductor length
Optimization of the cryo-distribution with (4.6 K, 0.48 bar) and a power saving of -33% with respect to reference case

## Slide 14: Comparative results- global optimization WP2
∆P (bar) | 1.0
Tinlet (K) | 4.05
Prefr, reference(W) | 217
Prefr, optimizedW) | 271
Power saving (%) | +25
Heat loads (W) | 167
Inter-turn and inter-layer impact the heat load distribution
Double layer DL5 is the most critical one: the Tmargin=1,5 K is located at the end of the conductor length
Optimization of the cryo-distribution with (4.0 K, 1 bar) and increase of the refrigeration power +25% with respect to reference case

## Slide 15: Comparative results – WP3 Pancake design
∆P (bar) | 0,20
Tinlet (K) | 4,3
Prefr, reference(W) | 387
Prefr, optimizedW) | 207
Power saving (%) | -46
Heat loads (W) | 164
Inter-turn impacts the heat load distribution  peak power in the first 50 meters of the conductor length where the temperature margin is located.
Optimization of the cryo-distribution with (4.3 K, 0.2 bar) with a power saving -46% with respect to reference case

## Slide 16: Comparative results – Summary
 | WP1 | WP2 | WP3
∆P (bar) | 0.48 | 1.0 | 0.20
Mass flows (g/s) | ~ 1700 | ~ 800 | ~ 1500
Tinlet (K) | 4.6 | 4.05 | 4.3
Prefr, reference(W) | 342 | 217 | 387
Prefr, optimizedW) | 229 | 271 | 207
Total Ideal Power Pideal, optimized (kW) | 402 | 403 | 328
Power saving (%) | -33 | + 25 | -46
Heat loads (W) | 186 | 167 | 164
The 3 TF designs have different optimized cooling parameters (Tinlet ,∆P)
It would induce different refrigeration requirements: refrigeration power but possibly could lead to different cryo-distribution and cryoplant architectures
The reference cooling parameters (Tinlet =4.5 K, ∆P=1 bar) are not the optimized parameters to minimize the refrigeration power.
  Some potential power saving of 30-45% have been estimated for WP1 and WP3.
  WP2 requires +25% refrigeration power in order to become compliant with the temperature margin of 1.5 K.

## Slide 17: Comparative results – Summary
Comparison between the reference and optimized cases
  Optimized WP1 (Tin=4.6 K, ∆P=0.48 bar)
    joint resistance is included in the heat loads
    Significant decrease of the cold circulator power
  Optimized WP2 (Tin=4.05 K, ∆P=1 bar)
    To become compliant with the 1.5 K temperature margin, the cold compressor pumping load is increased to pump down the temperature bath down to 4.05 K
  Optimized WP3 (Tin=4.3 K, ∆P=0.2 bar)
    Significant decrease of the cold circulator power
Details on the different contributions in the refrigeration power distribution
Reference cooling case
Tin= 4.5 K, Pin=6 bar,
= 1 bar
(ITER-like)

## Slide 18: Conclusions and perspectives
A methodology for optimizing the cooling parameters of the TF conductor ( ,)
  A 1D conductor model with thermal inter-turn and inter layer couplings allowing a good representation of the thermal hydraulic behaviour and heat load distribution.
  A cryo-distribution model to perform optimization calculation on in order to minimize the total refrigeration load, with a given temperature constraint on the temperature margin
The methodology has been applied on the 2015 DEMO TF designs WP1, WP2 and WP3
  The 3 TF designs have different optimized cooling parameters ( ,)
  The reference cooling parameters chosen for ITER and JT-60SA =4.5 K, =1 bar) have to be challenged in EU DEMO conceptual phase.
  There are potential interests to look at different cryo-distribution schemes which will open the investigations on the possible cryoplant architectures with available cryogenic components.
This methodology is relevant for the conceptual phase of EU DEMO to include the cryo-distribution and cryoplant analyses in the iteration loop dedicated to design the different options of conductor
  Further analyses have been initiated on the overall cost of the cryo-magnetic system, taking into account the mass of the conductors and the required refrigeration power

## Slide 19: Thank you for your attention Questions?