## Slide 1: Energetic particle instability characteristics of reactor-scale stellarators
September 30, 2026
19th Technical Meeting on Energetic Particles in Magnetic Confinement Systems
Oak Ridge National Laboratory
Collaborators: L. Garcia, Y. Ghai, J. Varela, A. Bader, A. Chambliss
Don Spong
Notes: Accessing Title Slide Options The standard ORNL presentation template includes five branded title slide layouts:
  Title | Standard. The preferred layout for lab-wide and general presentations. Features a default aerial photograph of the lab.
  Title | Custom Image. Allows replacement of the default background with a custom full-slide image (16:9 or 4:3 landscape format).
  Title | Custom Portrait Image. Supports inclusion of a custom 4:3 portrait image positioned next to the introductory text.
  Title | Custom Landscape Image. Supports inclusion of a custom 16:9 landscape image positioned next to the introductory text.
  Title | Text Only. Offers additional space for longer titles and multiple presenters.
Additional Lab-approved title slides specific to directorates and user facilities are available in PowerPoint under the following folders: Custom Title Slides and User Facility Templates, located in Presentation Templates.
Custom Title Slide Guidelines
  Image Rights. Any custom images, graphics, or photography must be owned by ORNL or used with documented permission from the original creator or source.
  Appropriate Image Use. Select images that work well with the layout. Ensure the focal point of the image is not obscured by the title text and white overlay box.
  Relevance and Impact. Visuals are a key element of effective communication. Whenever possible, use imagery that enhances the message of your presentation and reflects ORNL’s mission and values.
  Quality and Clarity. Use high-resolution images for clarity on large screens. Avoid overly complex or dark images that may conflict with the title text.
  Text-Only Option. If no appropriate or approved imagery is available, or if imagery is not permitted for the subject matter, the Title | Text Only layout provides a clean, professional alternative.
Learn more about ORNL presentations
  https://ornl.sharepoint.com/sites/Branding/SitePages/Presentations.aspx

## Slide 2: Stellarators offer unique opportunities for energetic particle physics issues. This talk will:
Introduce stellarators => symmetries, flexible design, optimization to a range of physics goals
Describe the gyrofluid approach to stellarator EP instability modeling
Demonstrate AE suppression at increased densities in stellarators => stabilization above ~2.5 x 1020 m-3 and Pfus < 1GW
Examine the nonlinear effects of instabilities: enhanced EP transport, zonal flow generation

## Slide 3: 3D systems have both external and hidden symmetries
External symmetries
Hidden symmetries – stellarators
  Transform to Boozer coordinates => GC orbit trajectories depend only on |B|
  |B| ~ f(ѱ,M𝛳-N𝜻) M = 0 (poloidal quasi-symmetry), N = 0 (toroidal quasi-symmetry), N/M = rational number (helical quasi-symmetry)
  Omnigeneity – drift optimization, piecewise omnigeneity => more flexibility than quasi-symmetry
Device | Field period symmetry | Reflection symmetry
Tokamak with ripple | Nfp ~ 18 | Nfp fold anti-reflection symmetry Flux surface covering field lines + islands
Tokamak with ripple + up-down asymmetry | Nfp ~ 18 | None
Tokamak with ripple + ferritic materials | Nfp ~ 1 to 3 | None
Stellarator | 1 < Nfp < 12 | Nfp fold anti-reflection symmetry Flux surface covering field lines + islands
Bumpy torus/square, Drakon | Nfp ~ 20 | Nfp fold reflection symmetry closed field lines – no islands

## Slide 4: Optimized stellarators strive for “hidden symmetries” to improve confinement => flux surfaces are not symmetric, but B in Boozer coordinates reduces to a 2D function
QH (helical symmetry example from Landreman, et al. (2022)

## Slide 5
From February, 2024 presentation by Dario Panici, “Stellarator Equilibrium and Optimization with DESC”

## Slide 6: Stellarators can be synthesized to achieve physics goals
Coils outer magnetic surface shape physics properties
3D shapes open up very large design space: ~ 40 independent parameters (A. Boozer, L. P. Ku, 2010) based on SVD analysis
Axisymmetric tokamak shape parameters: 𝜀, 𝜅, 𝛿
Thought experiment: quantize shape parameters into 10 levels
  103 2D configurations vs. 1040 3D configurations => “combinatorial explosion”
  Other large numbers: 7x1022 visible stars, 6x1030 prokaryotes (bacteria) on earth’s surface
STELLOPT, SIMSOPT,
DESC, ROSE, …
Adjust plasma
boundary
or coil geometry shape
Solve 3D
equilibrium
Calculate
𝝌2 (physics + engr. targets)
Levenberg-Marquardt
or other method used to minimize 𝝌2

## Slide 7: Stellarators have been successfully optimized for EP confinement issues
M. Landreman, et al. (POP, 2022) good alpha particle confinement in optimized stellarators
E. Paul, et al. (JPP, 2025) HAE gap narrowing by shape optimization
FAR3d based optimization of AEs initiated (2026), N. Ambadipudi, D. Spong, J. Larson:

## Slide 8: For 3D configurations the toroidal mode number (n) is not a good quantum number
Field period symmetry: Nfp replicated elements
Toroidal coupling => mode families, rather than single toroidal modes:
  n’ ± n = kNfp, k = 0, 1, 2, …
n = ±1 mode families
10 families
5 families
4 families
3 families
2 families
1 family
/DIII-D
Nfp=> ∞

## Slide 9: For 3D configurations the toroidal mode number (n) is not a good quantum number
Field period symmetry: Nfp replicated elements
Toroidal coupling => mode families, rather than single toroidal modes:
  n’ ± n = kNfp, k = 0, 1, 2, …
n = ±1 mode families
10 families
5 families
4 families
3 families
2 families
1 family
/DIII-D
Nfp=> ∞
W7-X
WISTELL-D

## Slide 10: Alfvén instability drive in stellarator reactors can potentially be mitigated by high density operation
Stellarators significantly exceeded the tokamak density limits
  LHD has demonstrated peak densities of ~ 4.5 x 1020 m-3
    Super-dense core regime, N. Ohyabu, T. Morisaki, et al., Phys. Rev. Lett. 97 (2006)
  W7-AS demonstrated ~ 3 x 1020 m-3
    HDH regime, R. Jaenicke, S. Baeumel, J. Baldzuhn, et al., PPCF 44 (2002).
Alpha slowing-down time inversely proportional to density
  high density shortens slowing-down time, lowers EP instability drive
However, stellarator designs tend toward higher aspect ratio
  At same fusion power output => smaller <a>, stronger 𝛼 gradients
Current optimized stellarators => low shear iota profile
Alpha physics tests: tokamaks => ITER, stellarators => ? Need to model AE stability boundaries vs. density

## Slide 11: The effect of increasing density: linear stability study of WISTELL-D along constant fusion power contours (D. Spong, et al. 2026 submitted to JPP)
Contours of constant fusion power => determine plasma density and temperature:
From steady-state slowing-down formulas Estrada-Mila, J. Candy, R. Waltz, Phys. Plasmas 13 (2006) all relevant alpha particle parameters are determined from ne, Te

## Slide 12: The parameter space for reactor EP instability studies is minimized by following constant fusion power contours
WISTELL-D, Pin = Pfus/5

## Slide 13: Iota and pressure profiles derived from the equilibrium, ne, Te inferred from pressure: ne = ne0 (p/p0)𝜹, Te = Te0 (p/p0)(1-𝜹), Ti=Te, 𝜹 = 0.3. Alpha parameters from slowing-down formulas
Rotational transform = 1/q
Equilibrium pressure (Pascals)
β𝛼 profiles

## Slide 14: AE drive weakens with increasing density along constant fusion power contours

## Slide 15: For the density scan study, we use the reduced dimensionality model FAR3d
Landau closures [as introduced by Hammett, Perkins (1990)] => linear fast ion resonance effects
Used in several other EP stability models (TAEFL, TGLF-EP, MAS)
Includes linear ion and EP FLR effects (Padé form), thermal ion/electron Landau damping, compressibility, 2-fluid option
Applied to tokamaks, stellarators, RFPs
Linear/Nonlinear options; initial value/eigenvalue options
  Nonlinear saturation - convective and JxB nonlinearities drive profile changes, zonal flows/zonal currents
Checked against other codes for tokamaks: S. Taimourzadeh (2019)
Review paper: J. Varela, D. Spong, et al., Frontiers in Physics (2024)

## Slide 16: Poloidal/toroidal mode number distribution: chose to provide dropoff in volume averaged kinetic energy => Dominance of high mode number range (m ~ 22, n ~ 25) in reactor regime
n = 1 mode family
n = 2 mode family
n = 3 mode family

## Slide 17: AE stability analysis indicates stabilization above densities of ~ 2.5 x 1020 m-3 for reactor power levels up to 1GW
Growth rates
Frequencies
Mode structures
n = 1
family
n = 2
family

## Slide 18: AE stability analysis indicates stabilization above densities of ~ 2.5 x 1020 m-3 for reactor power levels up to 1GW
Growth rates
Frequencies
Mode structures
n = 3
family
Key results from linear stability analysis:
For Pfus = 0.5 and 1 GW, growth rates are small or 0 above ne0 ~ 2.5 x 1020 m-3
For Pfus = 2 and 3 GW, instability remains up to highest density 5 x 1020 m-3
Mode structures localized in 𝜌/<a> ~ 0.4 to 0.7 interval
Frequencies in 𝜔real ~ 0.1 to 0.4 region

## Slide 19: The unstable AE modes reside in the Beta-induced Alfvén gap: suggests optimization methods should focus on this region
Region occupied by unstable modes
Alfvén continuum for the n = 3 mode family at ne(0) = 4.7 x 1020 m-3 and Te(0) = 12 keV

## Slide 20: Nonlinear simulations Reactor-scaled W7-X Wistell-D

## Slide 21: FAR3d nonlinear simulations (enlarged W7-X)
<B> = 5 Tesla, R0 = 22m, <a> = 2.1m, Volume = 1907 m3, Surface area = 2241 m2 Rescaled version of W7-X to reactor parameters

## Slide 22: Internal magnetic fluctuations at 4 different radial locations show 𝜹B𝛳/B0 in the range < 10-3, typical of experiments
Initial
phase
Exponential growth phase
Nonlinearly saturated phase
223 m/n modes are used and 400 radial grid points

## Slide 23
100kHz
50kHz
75kHz
10kHz
The magnetic fluctuations are FFT’d in a moving time window (spectrogram), indicating dominant frequencies

## Slide 24: Kinetic energy (perpendicular) evolution (volume-averaged)
Equilibrium (n = 0, 5, 15, 20) mode family

## Slide 25: 2D potential function slice at ζ = π/10 show a mode (m = 26 – 28) in linear regime that collapses down to m = 2 to 12 nonlinearly
t = 0.44 msec
t = 0.56 msec
t = 0.97 msec
t = 1.05 msec
t = 1.33 msec
t = 1.65 msec

## Slide 26: The evolving alpha density profile shows mild flattening in several regions due to AE-driven transport
local
flattening
local
flattening

## Slide 27: Fluxes can be derived from profile changes – flux gradient relations show nonlinear, non-diffusive nature of instability driven alpha transport
20 m2/sec
Non-diffusive transport can be modeled using integral kernel1 approach or ML surrogate2
1D. del-Castillo-Negrete, 2010 Nonlinear Process Geophys. 2Y. Ghai, arXiv:2606.15512
Alpha
Instability-driven flux
Flux-gradient relation

## Slide 28: FAR3d nonlinear simulations (WISTELL-D)
<B> = 8.1 Tesla, R0 = 10.1m, <a> = 1.25 m, 4 field periods, Volume = 439 m3, Surface area = 832 m2 - Reactor version of WISTELL-A

## Slide 29: Internal magnetic fluctuations at 4 different radial locations show 𝜹B𝛳/B0 in the range < 10-3, typical of experiments
Exponential growth phase
Nonlinearly saturated
phase
𝜹B𝛳/B0
𝜹B𝛳/B0
= Parameters for nonlinear case

## Slide 30: Spectrogram of frequencies at 𝝆 = 0.3 in nonlinear regime shows several modes coexisting
50kHz
110kHz
25kHz

## Slide 31: Magnetic energy (perpendicular) evolution (volume-averaged) shows n = 0 family driven by n > 0 modes
Equilibrium (n = 0, 4, 16, 20) mode family
1.1msec
0.5 msec

## Slide 32: 2D potential mode structure evolution indicates shearing and a collapse to lower mode numbers (m ~ 18 drops down to m = 2 – 4)
t = 0.18 msec
t = 0.37 msec
t = 0.55 msec
t = 0.78 msec
t = 0.82 msec
t = 1.0 msec

## Slide 33: The evolving alpha density profile shows mild flattening in several regions due to AE-driven transport
local
flattening
local
flattening

## Slide 34: Fluxes can be derived from profile changes – flux gradient relations show nonlinear, non-diffusive nature of instability driven alpha transport
10 m2/sec
Instability-driven flux
Flux-gradient relation
Alpha

## Slide 35: The zonal flow and zonal flow shearing rate show sustained amplitudes near 𝜌 ~ 0.3 and 0.7 near where the BAE mode induced density flattening was large.
Zonal flow velocity
Zonal flow shearing rate

## Slide 36: Nonlinear simulations for the power scan are underway – magnetic energy growth reflects linear growth rates
3GW
2GW
1GW
Equilibrium (n = 0, 4, 16, 20) mode family
Higher n’s (n = 17, 18,19, 21)

## Slide 37: Conclusions
Linear density scan (WISTELL-D)
Alfvén-stable regimes identified at ne0 ≥ 2.5 x 1020 m-3 for Pfus ≲ 1 GW; at 2–3 GW instability persists up to 5 x 1020 m-3
  Unstable modes in the BAE gap, localized at ρ/<a> ~ 0.4–0.7
  Stability boundaries depend on reactor configuration, magnetic field strength, and reactor size
Nonlinear simulations (reactor-scaled W7-X, WISTELL-D)
Many-mode saturated nonlinear simulations demonstrated, with δBθ/B0 < 10-3
Alpha particle and energy fluxes are non-diffusive and non-local
  A diffusive fit gives only a rough D ~ 10 m2/sec (WISTELL-D) to 20 m2/sec (reactor-scaled W7-X)
  ML surrogates or integral-kernel formulations needed in place of diffusion coefficients
Localized zonal flows are nonlinearly driven; shearing levels show they can supplement turbulence-driven zonal flows
Next steps
Nonlinear simulations of the 1–3 GW power scan are underway
Examine AE suppression by high density in other devices