## Slide 1
Panith Adulsiriswad
[1] National Institutes for Quantum Science and Technology, Naka Institute for Fusion Science and Technology
[2] National Institute for Quantum Science and Technology, Rokkasho Institute for Fusion Energy
19th Technical Meeting on Energetic Particles
Properties of Pressure-driven & EP-driven MHD Instabilities in Helical Core ITER-Scale Plasmas
September 30, 2026

## Slide 2
Helical core (HC)1 is a Long-lived ideal saturation state of kink/quasi-interchange mode.
  Observed in the tokamak hybrid scenario ( )
[1] Cooper, W. A., et al. Physical review letters 105.3 (2010): 035003
  Spontaneous formation is predicted in ITER2-3
[2] Wingen, A., et al. Nuclear Fusion 58.3 (2018): 036004
[3] Cooper, W. A., et al. Plasma Phys. and Cntrl. Fusion 53.2 (2011): 024002
  Responsible for the poloidal flux-pumping4
    Sawtooth-free plasmas with expense toroidal symmetry
[4] Piovesan, P, et al. Plasma Phys. Cntl Fusion 59.1 (2016): 014027
Using kinetic alpha + MHD model (MEGA) to study HC formation in ITER-scale plasmas, we found that5
1. Fusion-born alphas enhances HC displacement ()
2. Within , alphas remain well-confined* * Caveat: However, the effects of other instabilities in the HC equilibrium have not be assessed!
HC axis Displacement (m)
MEGA & VMEC agree within
[5] P. Adulsiriswad et al. Nuclear Fusion 66.4 (2026) 046032
    Background : Helical Core Formation in Tokamak Plasmas

## Slide 3
    Research Motivations & Objectives
1) Previously, the effects of EP-driven instability were not considered
  Limit to harmonics and HC formation phase
Source: D. Spong, ORNL, APS 56th Annual Meeting
DIII-D TBM Exp.
Motivations
“To verify the feasibility of a HC-based tokamak reactor, its stability need be assessed.”
How HC toroidal asymmetry affects MHD stability?
Question 1:
If there is an instability, how critical is it?
Question 2:
In LHD, n=1,9,11,19,21 are the same mode
2) Toroidally Asymmetry1 leads to loss of mode degeneracy
[1] Spong DA, et al. Physics of Plasmas 10.8 (2003): 3217-3224.
[2] Kolesnichenko YI, et al. Physics of Plasmas 9.2 (2002): 517-528
  “n” harmonic is coupled with “
    More wave–particle resonant channels2
    In HC (Nfp=1), all “n” constitute to a same family
& HC

## Slide 4
Calculation Basis, Assumption, Setups

## Slide 5
q
%
    Calculation Assumptions & HC Equilibrium
Magnetic Field Strength in Lab Frame
ITER-scale hybrid scenario
  Scan , , and
Assumptions: 1) Static HC Equilibrium 2) Negligible transport during HC Formation
The HC equilibrium state calculated with VMEC1-2
[1] Hirschman S.P., et al. Phys. Fluids 26 (1983) 3553
[2] Cooper, W. A., et al. Physical review letters 105.3 (2010): 035003
Experiences different B
Slightly Asymmetric
At , X-axis is inverted.

## Slide 6
MEGA1, a global nonlinear kinetic PIC MHD simulation code, is used in this work.
  Simultaneously solves full MHD equations & drift kinetic equation for energetic particles
[1] Todo, Y. et al. Phys. of plasma 5.5 (1998): 1321-1327
Cylindrical Grid Resolution
  Inherently poor core resolution
  We only simulate the core region () area
      (,)=(200,256,200) ( , )=(400,256,400) ( , )=(200,512,200)
Dissipation Coefficients
  1) Study of Pressure-driven MHD Instability
  2) Study of EP-driven MHD Instability
Higher dissipation is used to stabilized pressure-driven mode
Convg. Test
  *Model is nonlinearly, but our study is limited only to the linear growth phase
    Simulation Model & Parameters
Mass Diffusivity
Thermal Diffusivity
Resistivity
Viscosity
Normalized
Energetic Particles
  Slowing-down Fusion-born Alphas

## Slide 7
Pressure-Driven Magnetohydrodynamics Instability in HC Plasmas
Simulation Parameters
:

## Slide 8
    Eigenfunctions of HC-induced MHD Instability (I)
Cylindrical Coordinate
Short-wavelength mode is found to be unstable in HC equilibrium.
  Localized along the HC compressed flux region
Compressed Flux Region
Compressed Flux Region
Compressed Flux Region
Compressed Flux Region
Stable in the axisymmetric equilibrium (Same and ) (Only the m/n=1/1 and 2/2 modes are unstable)
At first glance, mode seems to have mixed parity
Fourier Representation
Consists of a broad harmonic spectrum
  Difficult to comprehend
*See Appendix for discussion via Fourier mode
Tearing –like parity
Interchange parity
Interchange parity
Interchange parity
“We found an interchange parity mode localized along the HC compressed flux region”
Key Message:
Tearing-like parity emerges from the incomplete cancellation of adjacent interchange-parity harmonics

## Slide 9
    Eigenfunctions of HC-induced MHD Instability (II)
“HC-induced mode intrinsically has a long , delaying the global coherence formation”
Key Message:
Generalized Toroidal Angle
Generalized Poloidal Angle
(2) Each peak exchanges information via SAW at the rate of
Can be very slow!
(1) Long connection length
|q-1|0 is intrinsic
  .9 for this case (More Ex. in Appendix)!
(3) A global coherence may not fully develop if
Along the Field Line
(2) Exchange phase info at rate
(1)
HC Compressed Flux ( Grow independently at t=0 )
(3) Sensitive to initial perturbation Random Seed Scan

## Slide 10
Resistivity Scan
Its resistive dependence resembles that of a ballooning mode
Bulk Plasma Pressure Scan
Fixed & HC Structure
“This mode is driven by ”
    Dependence of HC-induced Instability on Bulk Plasma & Resistivity
Weakened field line bending
Bypass field line bending
Resistive Branch1
Fast Branch1-2
Ideal
Branch
“The underlying physics of the HC-induced mode may be associated with the ballooning mode”
Key Message:
Confirms that this mode is driven by
*Completely stabilize with an artificially flat
[1] L. Garcia., et al., Phys. Plasmas 6 (1999), 107-115
[2] B.A. Carreras., et al., Phys. Fluids 30 (1987), 1388

## Slide 11
Energetic Particle-Driven Magnetohydrodynamics Instabilities in Helical Core ITER Plasmas
Simulation Parameters
:
“To suppress Pressure-driven Mode”

## Slide 12
    Linear Properties of EP-driven Mode
=18
=
Peak harmonic
m/n =
m/n=n+2/n BAE-CAP
m/n=n+1/n BAE-CAP
Mode resides at the BAE-CAPs
Continua were calculated using the modified STELLGAP (Implement up-down asymmetry)
  Continua
Even when the pressure-driven mode is stabilized, alphas can still drive a mode with similar structure
  In the axisymmetric eq., this mode is stable.
“Alphas can drive a mode that resides at the BAE-CAP, but its identification remains inconclusive”
Key Message:
m/n=(n+1)/n Clusters
(n+2)/n Clusters
m/n=34/33 & 35/33

## Slide 13
    AE-like Dependence of the Mode Frequency on Electron Density
=0.5
=0.75
=1.25
Vary only
Performed scan, while fixing pressure
Mode frequency scales inversely with - BAE-associated mode - Frequency is governed by MHD plasmas
0.5nb 1.25nb
Fixed =1% and ==

## Slide 14
    AE-like Dependence of the Mode Properties on Alpha Birth Energy
“Both sensitivity analysis suggests that this mode is likely to be associated with BAE”
Key Message:
450 keV 7800 keV
7800 keV
450 keV
900 keV
1800 keV
5300 keV
Investigate frequency dependence on to confirm BAE-associated mode 450 keV Ebirth 7800 keV *Contrast of -f diagrams were reduced
Only ~20% across or - BAE-associated mode
~200% across or - EPM?
3540 keV

## Slide 15
Exact resonances are marked with
Magnetic Midplane
HC Region
Axisymmetric Region
    Why can HC induce a short-wavelength EP-driven mode?
We analyze the unperturbed orbit of the alphas along the magnetic midplane
Poloidal Sideband
28 kHz
Toroidal Sideband
High-n sideband resonances are spatially overlap at the mode location
High-n harmonics synchronize and simultaneously grow
=40
High - n sidebands are spatially overlap
High - n sidebands are spatially overlap
=1
This short-wavelength BAE is not observed in the axisymmetric equi. Why?

## Slide 16
    “Preliminary” Nonlinear Results
During the nonlinear phase, the long-wavelength mode also becomes unstable.
Mode Energy Evolution
Mode Structure & Frequency
m/n=2/2
m/n=1/1
t=0
t=985
Short-wavelength BAE
Long-wavelength Mode
Within the capability of our model, this mode leads to a minor transport of fusion-born alphas in our ITER-scale plasmas
Caveats: - Mode stability/scale length is sensitive to the dissipation coefficients
“A higher-fidelity physics model is needed to resolve the small-scale physics and dissipations, and to confirm this low-alpha transport”
Key Message:

## Slide 17
Conclusion & Outlook

## Slide 18
    Conclusion / Outlooks
18
Outlooks
&
Key Challenges
Quantitative assessment of HC stability requires a higher fidelity physics
Multi-scale (global) EM 3-D gyrokinetic simulation
2. Spectral method is ill-suited because a broad harmonic spectrum must be simultaneously considered
Grid-based solver?
3. Straight field line coordinate has a geometrically complex metric coefficients in HC equilibrium
Limit to a small HC study?
Z (m)
R (m)
Q1) How HC toroidal asymmetry affects MHD stability?
  Ideal/resistive PRESSURE-driven MHD mode
  Weaken field line bending/change in curvature?
  ii) Low-frequency BAE-associated mode.
  High-n Linear resonance overlap
HC can induce a helically localized short-wavelength
Slow formation of the global coherence structure
|q-1|0 is intrinsic for HC
Q2) How critical is it?
Within our model, the alpha transport remains small, BUT mode stability, saturation, and scale length are sensitive to dissipation coefficients
  Higher-fidelity physics model is needed for a quantitative assessment
Generalized angle is strongly distorted

## Slide 19
    Peculiar Effects of Dissipation & Bulk Pressure on Mode Properties
- Scan
Fixed =1%
Mode is stabilized at low- for 10-5
Weaken HC compression & asymmetry?
Gap changes?
=
★ =5
Pressure - driven mode dominates
Sound Continua may be affected by ? or the mode transits to EPM?
Frequency slightly reduces

## Slide 20
    Appendix: Sensitivity of Mode Structure on Initial Condition
Z (m)
Z (m)
The only difference is the random number seed for generating the initial perturbation.
The macroscopic structure and growth rate are similar, but the fine structures are not.

## Slide 21
    AE-like Dependence of the Mode Properties on Alpha Pressure & Energy
Mode is driven by alphas
0.5 Scan
Fixed =6.5%
Same Mode
Mode frequency is defined by background plasmas
450 keV 3540 keV
“Sensitivity analysis suggests that this mode is likely to be associated with BAE”
Key Message:

## Slide 22
    Visualization of HC Equilibrium in Real Space
Magnetic Axis
Axisymmetric Equilibrium
Above
Original axis
Below
Original axis
HC Equilibrium
Toward LFS
(Larger Volume)
Toward HFS
(Smaller Volume)
HFS
LFS
HFS
LFS
HFS
LFS
HFS
LFS
*X-axis is inverted!
“Pressure profile is steepened along the compressed flux region”

## Slide 23
    Appendix: MHD Continua in HC Equilibria
HC Equilibrium
Axisymmetric Equilibrium
At gap point, high-n continua merges
Each ‘n’ has a unique continuum
Continua were calculated using the modified STELLGAP (Implemented Up-down asymmetry)
Each color represents each unique “n”

## Slide 24
Appendix 1
    Poloidal & Toroidal Convergence Tests
Base Case
(,)=(200,256,200)
Poloidal Convg. Test
(,)=(400,256,400)
Toroidal Convg. Test
(,)=(200,512,200)
=
=
=

## Slide 25
    Appendix: Eigenfunctions of HC-induced MHD Instability (Fourier Space)
All Harmonics
Magnetic Shear Inversion Radius
This mode consists of a broad spectrum of “n” & “m” Fourier harmonics
Two clusters
interfere Constructively
LFS of =
Two clusters
interfere Destructively
HFS of =
  Consists of two clusters: m/n= (n+1)/n & (n+2)/n
  Difference in parity is due to “poloidal coupling”
“These cannot yet explain helically-localized structure”
m/n=(n +2)/n Cluster
m/n=(n +1)/n Cluster

## Slide 26
    Phase Analysis of HC-induced Instability
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
=
=9
=1
=2
“A single n harmonic is insufficient to explain the helically localized structure”

## Slide 27
    Phase Analysis of HC-induced Instability
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
=
=9
=1
=2

## Slide 28
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
    Phase Analysis of HC-induced Instability
=
=9
=1
=2

## Slide 29
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
    Phase Analysis of HC-induced Instability
=
=9
=1
=2

## Slide 30
    Phase Analysis of HC-induced Instability
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
=
=9
=1
=2

## Slide 31
    Appendix: Phase Analysis of HC-induced Instability
  To understand mode helical localization, we analyze the phase of each toroidal harmonic
=
=
=
=
n=52 Poloidal Structure
=
=
=
=
164 Poloidal Structure
=
=9
=1
=2
“This pressure-driven mode may be a cluster of weakly unstable ‘n’ ballooning modes coupled by HC”
Perturbations are cancelled out
Constructively Interfere

## Slide 32
    Appendix: Time Evolution of the Eigenfunction (Reference Case)
t= ms 87/
t= ms 62/
t=4.96 ms 47/
Shear Alfven wave takes roughly / time to propagate/communicate between each peak.
  Eigenmode structure can partially develop.

## Slide 33
    Appendix: Effects of Viscosity on Mode Eigenfunction
Mode structure becomes smoother
  *Caveat: Broadening caused by viscosity may intertwine with decorrelation!

## Slide 34
    Appendix: Sensitivity of Mode Structure on Initial Condition
Z (m)
Z (m)
The only difference is the random number seed for generating the initial perturbation.
The macroscopic structure and growth rate are similar, but the fine structures are not.

## Slide 35
Peak harmonic
m/n=
    Appendix: Linear Properties of EP-driven Mode
Alphas drive HC localized mode, residing at the BAE-CAPs
Continua were calculated using the modified STELLGAP (Implemented Up-down asymmetry)
1 n 40 Continua
m/n=(n+2)/n Continua
Axisymmetric Equi. Counterpart
High-n modes are stable
m/n=1/1 f~1.05 kHz
m/n=2/2
f~3.14 kHz
m/n=3/3
f~5.7 kHz
Only long-wavelength low-frequency EPMs are unstable
[1] ZZ Ren et al 2017 Phys. Plasmas 24, 052501
[2] S Liu et al 2024 Phys. Scr. 99 075604
=18
=

## Slide 36
    Appendix: Pressure-Driven Mode Stability in Axisymmetric Equilibria
(b) =1.10/
n=1
m/n=1/1
(b1)
(b2)
(b4)
(b3)
(a) =1.02/
m/n=1/1
m/n=2/2
(a1)
(a2)
(a4)
(a3)
n=1
n=2