## Slide 1: Overview of energetic particle physics studies on TCV
Anton Jansen van Vuuren, M. Podestà, A. N. Karpushov, M. Rud, Q. Kernel, A. Fasoli, D. Mykytchuk J. Poley-Sanjuán, B. P. Duval, J. Decker, B. Rofman, M. Dreval, S. Sharapov, and the EUROfusion Tokamak Exploitation* and the TCV** teams
* See author list of N. Vianello et al 2026 Nucl. Fusion 66 116010
** See author list of C. Theiler et al 2026 Nucl. Fusion 66 116007
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.

## Slide 2: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbone redistribution of fast-ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 3: The Tokamak à Configuration Variable (TCV)
See C. Theiler et al 2026 Nucl. Fusion 66 116007
Major and minor radii | 0.88 / 0.25 m
First wall material | Carbon (graphite)
Max magnetic field | 1.54 T
Max plasma current | 1.0 MA
Max elongation | 2.8
Triangularity | -0.6 / +0.9
Pulse duration | 2 s (4 s)
ECH power | 2.4 MW – X2 +1.9 MW – X3
NBI power | 2.5 MW
Main species | D, H, He

## Slide 4: TCV offers exceptional plasma-shaping flexibility
    16 independently controlled poloidal-field coils enable a wide range of plasma shapes and magnetic configurations.
    Enables systematic investigations of plasma-shaping effects on particle confinement.

## Slide 5: TCV combines flexible ECRH and NBI heating capabilities
Neutral Beam Injection (NBI)
Diagnostic beam: 50 keV H, 70 kW
NBI1: 28 keV, up to 1.3 MW [1]
NBI2: 55 keV, up to 1.3 MW
TCV Top View
Electron Cyclotron Resonance Heating (ECRH)
X2: Three real-time steerable launchers, up to 2.5 MW
X3: Two launchers, up to 1.9 MW
[1] A. Karpushov et al., 2023, Fusion Engineering and Design, 187, 113384
    NBIs generates ions with velocities approaching vA/3, providing drive for Alfvén eigenmodes (AEs).
    Near-Alfvénic velocities (v∼vA) are accessible at reduced magnetic field (Bt ≈ 0.9 T).
TRANSP
Fast-ion Distro.

## Slide 6: TCV is equipped with a comprehensive suite of fast-ion diagnostics
Several diagnostics provide measurements of fast-ion confinement and losses :
Fast-ion loss detector (FILD)
Supported by an extensive suite of plasma diagnostics, including charge-exchange spectroscopy (CXRS), Thomson scattering, as well as fluctuation diagnostics
Fast-ion D-alpha spectroscopy (FIDA)
Neutron detector (1MHz)
Ion cyclotron emission (ICE) probes
TCV Top View
TRANSP
Fast-ion Distro.

## Slide 7: TCV features a unique Fast-Ion Loss Detector (FILD)
    Four slits enable measurements for all Ip and Bt combinations [1].
[1] J. Poley-Sanjuán et al 2025 Nucl. Fusion 65 076006
    Rotatable head allows precise alignment with the edge magnetic field [2].
[2] J. Poley-Sanjuán et al 2025 Rev. Sci. Instrum. 96 083504
    Reconfigurable APD array enables velocity-space mapping across four configurations.
    Dual acquisition: 3 kHz camera and 128-channel APD array (up to 4 MHz).

## Slide 8: High-resolution measurements of fast-ion losses in velocity space
    Remapping of CMOS and APD signals enables high-resolution velocity-space measurements.
Conditional ELM averaging (5 cycles)
[1] J. Poley-Sanjuán et al 2025 Nucl. Fusion 65 092006
[2] J. Poley-Sanjuán et al 2026 Nucl. Fusion 66 036009
    Tomographic reconstruction of the velocity distribution at the pinhole currently being implemented. See presentation by Q. Kernel on Friday morning and poster by M. Larsen Thursday
    Energetic-ion loss dynamics resolved with unprecedented detail [1, 2].
APD views
FILDSIM
Strike map

## Slide 9: FIDA spectroscopy probes the confined fast-ion distribution
Vertical FIDA
Horizontal FIDA
    FIDA spectroscopy probes the confined fast-ion distribution.
[1] M Rud et al 2026 Plasma Phys. Control. Fusion 68 015035
Bayesian velocity-space tomography enables reconstruction with uncertainty quantification [1] see M. Rud’s poster on Thursday 
Top and midplane views, with a third bottom view planned.
Doppler shifted emission contains information on confined fast-ion distribution.
Evaluate theoretical the fast-ion distribution against measured spectra via forward modelling.

## Slide 10: ICE probes routinely measure ion cyclotron emission on TCV
    Two orthogonal magnetic probes installed in 2024, measuring two components of the fluctuating magnetic field [1, 2].
[1] A. Jansen van Vuuren et al 2026 Nucl. Fusion 66 086033
[2] R. Ochoukov et al 2026 EPJ Web of Conferences 346 03009
    High-speed acquisition with 1 GS/s sampling rate over full shot duration.
    ICE routinely observed, predominantly at the second ion cyclotron harmonic.
[3] B. N. Breizman et al 2025 Phys. Plasmas 32 100702
    A new interpretation of TCV ICE suggests an origin in Bernstein-type shear Alfvén waves [3].

## Slide 11: ICE diagnostic upgraded with five additional toroidal probes
    Five new BZ probes installed in 2026, forming a toroidal array.
    Simultaneous acquisition at 1 GS/s.
    9 distinct angular separations (4.4°to 45°) were selected to enable toroidal mode-number determination.
    In-vessel calibration performed in summer 2026 to characterize frequency response and relative channel phases.
In-vessel calibration setup
Ex-vessel wave source
Single loop antenna
    Exploitation to start in current campaign

## Slide 12: Fluctuation diagnostics for mode characterization
    Magnetic pickup coils and ECE other fluctuation diagnostics provide complementary measurements of MHD activity and mode characteristics.
    Multichannel SXR diagnostics provide spatial information, enabling reconstruction of mode structures and radial dynamics [1].
    Combined measurements and modelling reveal complex EGAM and axisymmetric Alfvén eigenmode structures [2, 3].
[1] M.B. Dreval et al 2025 Nucl. Fusion 65 016037
    New MSE diagnostic (2026) to provide additional constraints on the q-profile for improving equilibrium reconstruction
[2] M.B. Dreval et al 2026 Plasma Phys. Control. Fusion 68 082501
[3] M.B. Dreval et al 2026 Nucl. Fusion 66 086025

## Slide 13: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbone redistribution of fast-ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 14: Integrated modelling workflow for fast-ion studies on TCV
    Experimental data combined with ASTRA, TRANSP and ASCOT simulations to assess fast-ion transport.
    Synthetic diagnostics enable direct comparison with FIDA, neutron and FILD measurements.
    MISHKA/FAR3D/ORB5 support interpretation of energetic-particle-driven instabilities.
    RABBIT is being implemented for real-time/control applications, but is not yet routinely used for fast-ion studies.
    Reduced transport modelling ORBIT + TRANSP kick model to investigate instability-induced fast-ion transport. [1] See presentation by M. Podesta on Friday morning 
[1] M Podestà et al 2017 Plasma Phys. Control. Fusion 59 095008

## Slide 15: TRANSP modelling integrated into the TCV analysis environment
    TRANSP runs on TCV analysis servers via docker with an easy interface for input preparation, simulation execution and analysis.
    Simulations are compared with experimental measurements, including stored energy and neutron rate
#89865
A.Y. Pankin et al 2025 Computer Physics Communications 312 109611
    Two principal mechanisms are considered: - Charge-exchange (CX) losses with background neutrals - MHD induced fast-ion transport
    Separating these contributions requires an independent constraint on the background neutral density.
    Reproducing experimental measurements requires significant fast-ion losses and/or redistribution.
#89865

## Slide 16: CX losses constrained using spectral measurements
    FIDASIM predicts thermal Dα emission using TRANSP neutral-density profiles.
Danom,FI2.5 m2/s
    Background neutral density is adjusted to reproduce measured Dα spectra, constraining the CX loss contribution.
    The remaining discrepancy is modelled using an ad-hoc fast-ion diffusion, Danom,FI, adjusted to reproduce experimental measurements.
Neutron rate
+ FIDA emission matched
    Both absolutely calibrated neutron rate and FIDA spectra matched

## Slide 17: ASCOT modelling of fast-ion losses and synthetic FILD signals
    ASCOT5 orbit-following simulations model fast-ion confinement and wall losses using realistic TCV equilibria and wall geometry.
    Fast-ion slowing-down distributions can be calculated, including the effects of charge-exchange (CX) losses.
    Synthetic FILD simulations predict fast-ion losses reaching the detector for comparison with measurements.
[1] J. Poley-Sanjuán et al 2025 Nucl. Fusion 65 092006

## Slide 18: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbones redistribution of fast ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 19: Comparable fast-ion confinement in quiescent NT and PT plasmas
    Matched NT/PT scenarios with identical NBI parameters and minimal MHD activity have been investigated [1, 2].
δ ~ -0.3
δ ~ +0.3
NT: 80323
PT: 80326
    TRANSP (and ASCOT) modelling successfully reproduce experimental measurements using neoclassical fast-ion transport.
    Charge-exchange (CX) losses are identified as the dominant fast-ion loss mechanism.
    Similar fast-ion confinement in comparable quiescent NT vs PT plasmas
Magnetics
    Differences in neutron rates are primarily attributed to thermal plasma conditions.
[1] A. Jansen van Vuuren et al 2024 APS-Atlanta
[2] J. Poley-Sanjuán et al 2026 Nucl. Fusion 66 046012
NT: 80323
PT: 80326
t = 0.54s

## Slide 20: Energetic-particle-driven instabilities differ between NT and PT plasmas on TCV
[1] M.A. Van Zeeland et al 2019 Nucl. Fusion 59 086028
    MHD-active NT and PT scenarios developed to investigate instability-driven fast-ion transport.
TAE
TAE
    eGAMs are more prominent in NT, but can be suppressed using localised ECH.
    Higher-amplitude TAEs and larger fast-ion losses observed in PT, unlike DIII-D experiments reporting comparable AE-induced transport [1].
    Modelling remains sensitive to plasma equilibrium inputs, particularly the poorly constrained experimental q-profiles.
ORB5
    Modelling predict higher TAE growth rates and amplitudes in PT, respectively [2, 3].
[2] Y. Ghai et al 2021 Nucl. Fusion 61 126020
[3] P. Oyola et al 2024 APS-Atlanta
    Further experiments with co-NBI planned to investigate these differences.
Note scale diff

## Slide 21: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbones redistribution of fast ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 22: A reproducible co-NBI scenario enables systematic AE control studies
Neutron rate
Magnetics
Toray
FILD
FILD retracted
NBI1
ECRH
ne
TAEs
n-number
    Previous TCV AE studies predominantly relied on counter-NBI scenarios [1].
    A reproducible, steady-state high power co-NBI scenario was established using off-axis ECRH, outside ρ ≳ 0.6.
    Strong TAEs are routinely excited that efficiently expel fast-ion.
    CX-constrained TRANSP modelling indicates anomalous fast-ion diffusion of Danom,FI around 2.5 m²/s, with even higher values inferred at increased ECRH power.
[1] A. Jansen van Vuuren et al 2026 EPS-Edinburgh

## Slide 23: TAEs are suppressed by on-axis ECRH deposition on TCV
    As ECRH deposition moves inward towards ρ ≈ 0.6, TAE amplitudes decrease and a lower-frequency mode, possibly a BAE, becomes dominant.
    With further inward deposition, coherent mode activity is suppressed and the neutron rate reaches its maximum.
Magnetics
FILD
Neutron rate
NBI1
ECRH
Toray
Launcher angle
ne
TAEs
BAEs
[1] S. E. Sharapov et al 2018 PPCF 60 014026
    Similar deposition-dependent behavior has been reported on ASDEX Upgrade, where off-axis ECRH destabilized TAEs driven by ICRH-accelerated ions [1].

## Slide 24: ECCD-induced shear changes possible explanation to suppression
Counter ECCD
CO-ECCD
    MSE measurements, however, indicate differences in the experimental shear profiles, suggesting sensitivity to small changes not captured by current modelling.
    Comparable observations on KSTAR and AUG highlight the influence of ECCD-induced equilibrium changes and the balance between energetic-particle drive and damping [1, 2]
    Co-/counter-ECCD scans reveal a moderate effect, consistent with the small driven (IECCD≈ ±5 kA vs IP ≈ 120 kA)
    Co-ECCD reduces TAE activity, while counter-ECCD has little effect.
    Modelling predicts similar fast-ion density and magnetic shear profiles for both configurations.
[1] Kim et al., Nucl. Fusion 2022 62 026029
[2] Calado et al., Nucl. Fusion 2024 64 016039

## Slide 25: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbone redistribution of fast ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 26: Fishbones trigger coherent bursts ​of fast-ion losses
    Scenario with fishbone instabilities well established on TCV.
    Magnetic perturbations and enhanced losses are well correlated​.
Magnetics
FILD
ICE
    Simultaneous burst of 3rd harmonic ICE observed corelated with
    Strong evidence radial expulsion of fast-ions to edge of plasma
See presentation by Q. Kernel on Friday morning 
Radial outward transport
Magnetics
FILD + Neutrons
FILD
Magnetics
ICE

## Slide 27: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbone redistribution of fast ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 28: TCV research on runaway electrons
    TCV is very active in runaway electron (RE) research with a multi-tier mitigation approach
[2] U Sheikh et al 2024 Plasma Phys. Control. Fusion 66 035003
    Expel RE seed using ECRH [1] ⟹ combined effects of heating and turbulent transport
    Limit RE beam current by increasing RE transport using inductively loaded mitigation coil (REMC) ⟹ will be installed on TCV in a few months See talk by A. Battey Friday morning
    inject low-Z gas to reduce the impact of the final collapse ⟹ “benign termination” resulting from fast-growing MHD mode and reduced RE regeneration [2]
    TCV is equipped with dedicated RE diagnostics: Bremsstrahlung diagnostics: PMTX, HXRS, BGO and recently LaBrDORE [3]
    Antennas capturing RE-driven kinetic instabilities: REWS (EPS-2026), recently upgraded ICE, future LHPI See poster by O. Panico 
[1] J. Decker et al 2024 Nucl. Fusion 64 106027
[3] Simons et al 2025 Rev. Sci. Instrum. 96, 093501 (2025)
[4] J. Poley-Sanjuán et al 2025 Nucl. Fusion 65 114001
    Fast-ion and electron detector [4]

## Slide 29: Investigating high-frequency instabilities associated with runaway electrons
    Automated mode-tracking algorithm developed to identify high-frequency (HF) modes measured by ICE probes
Out of 69 shots, 20 exhibited modes
    69 RE discharges analyzed, with HF modes identified in 20 discharges. Similar to RE modes seen on DIII-D [1, 2, 3]
    Modes appear during high HXR emission, with some dependence on plasma triangularity and temperature
    Mode-pair frequency spacing exhibits a strong inverse correlation with plasma density.
    Ongoing investigation to identifying the underlying wave physics (i.e. Whistlers [1,2] vs Ion Bernstein Waves [3])
[1] D.A. Spong et al 2018 Phys. Rev. Lett. 120, 1550021
[2] W.W. Heidbrink et al 2019 Plasma Phys. Control. Fusion 61 014007
[3] A. Lvovskiy et al 2019 Nucl. Fusion 59 124004
[4] W. Bin EPS Edinburg 2026
[5] C. Castaldo et al 2024 Nucl. Fusion 64 086003

## Slide 30: Outline
    TCV as a fast-ion testbed
        Heating and fast-ion sources
        Fast-ion diagnostics
    TCV Modelling and analysis workflow
    Recent energetic-particle studies on TCV
      Negative vs positive triangularity confinement
      Alfvén eigenmode control
      Fishbone redistribution of fast ions
      Runaway-electron and high-frequency waves
    Conclusions and outlook

## Slide 31: Conclusions
TCV provides a versatile testbed for energetic-particle studies, combining flexible heating, advanced diagnostics and integrated modelling.
Large suite of diagnostics enable detailed phase-space characterization of fast-ion populations.
NT and PT plasmas exhibit comparable neoclassical fast-ion confinement, but differences in AE activity and associated losses.
AE control experiments demonstrate effective TAE suppression using localized ECRH, with additional sensitivity to ECCD-induced equilibrium changes.
Fishbone instabilities produce coherent bursts of fast-ion losses, accompanied by ICE activity.
Other studies:
Structure and dynamics of n=0 modes, including eGAMs See posters by D. Banerjee, L-G Erickson, S. Cavallero and talk by F. Porcelli.
Interplay between supra Alfvénic fast ions and Alfvén eigenmodes
Interplay between AEs and turbulence during improved-confinement regimes.

## Slide 32: Outlook
Long-term goal: High-resolution characterization of fast-ion phase space to understand and ultimately control fast-ion transport and losses.
Leverage diagnostic upgrades:
ICE: Exploit the new toroidal array for mode-structure analysis.
MSE: Better constrain the core q-profile for equilibrium reconstruction and stability modelling.
Developing a new iNPA system for additional measurements of confined fast ions.
Extended stability modelling: Identify instability mechanisms and improve understanding of AE suppression and fast-ion redistribution.
Open to collaborations on both experimental and modelling activities!

## Slide 33: THE END
Thank you for your attention!

## Slide 34: Neutron detector
    TCV is equipped with a fast scintillator (6Li in ZnS(Ag) ) based neutron detector
    The detector operates at 1MHz and can resolve changes in neutron flux rates due to MHD mode activity.
    The fast detector is cross-calibrated against a slow (50ms) calibrated LUPIN neutron detector.
HDPE (50 mm)
Fresnel Lens
mirrored surface
filter
SiPM:
Ketek PA3325-WB-0808
HDPE
SiPM
neutrons from TCV