## Slide 1
Self saturation of Alfvén eigenmodes
with a reactor-like low ρ*
E.M. Bass and C. Holland
Presented at
IAEA Technical Meeting on Energetic Particles in Magnetically Confined Systems
Lausanne, Switzerland
September 28 – October 2, 2026
Supported by US DOE SMARTS and FREDA SciDACs
Computations performed at NERSC
UC San Diego
SMARTS
…toward refinement of the reduced TGLF-EP+Alpha model

## Slide 2: Outline
Background: The state of TGLF-EP+Alpha modeling
Nonlinear physics of stiff Alfvén eigenmodes in GYRO
Effect of decreasing r* (increasing mode density) on a test compact reactor scenario in nonlinear CGYRO

## Slide 3: TGLF-EP+Alpha: simple physics-based model for predicting energetic ion transport by Alfvén eigenmodes (AEs).
Inputs
  Complete equilibrium geometry
  Thermal-species profiles
  Source rate(s) or classical EP profile(s)
Outputs (steady-state)
  EP density profile(s).
  Radial density flux(es) versus radius.
  Revised power depositions.
Alpha: 1D radial energetic particle (EP) steady-state (time-invariant) density transport model includes:
Transport
AEs using critical gradient
Various models for (generally small) microturbulent EP transport
Sources/Sinks
Fusion or beam source
A sink representing slowing down collisions
TGLF-EP: Parallelized and automated wrapper for TGLF (local,
linear, thermal distribution) giving AE critical gradient
Major approximation: “Infinitely” stiff AE transport.

## Slide 4: The TGLF-EP+Alpha stiff EP transport model by AEs is now well integrated into modeling.
Collins et al. IAEA 2021
TGLF-EP+Alpha works well in many DIII-D discharges.
Integrating EP power redistribution into TGLF power predictions has become increasingly automated.

## Slide 5: TGLF-EP+Alpha has been applied to reactor scenarios
C. Holland et al., JPP 89, 905890418 (2023)
Holland compact reactor use case scenarios
Pulsed (UCP)
10% power loss
Steady state (UCSS)
65% power loss
Ti collapse results from loss of geometrical stabilization from alphas.

## Slide 6: The stiff transport assumption in TGLF-EP+Alpha is based on nonlinear GYRO simulations at modern experimental r*.
E.M. Bass and R.E. Waltz, PoP 17, 012319 (2010)
E.M Bass and R.E. Waltz, PoP 24, 122303 (2017)
Multiscale simulations included both AEs and microturbulence.
Simulation runaway signifies profile flattening is needed to saturate.
DEP/cgB per mode
kqrs
nEP/ne=0.5%
nEP/ne=0.8%
kqrs 0.8
AE range
AEs are just for 4 out of 40 modes in these multi-scale simulations.
Implication: Profiles must flatten down to the runaway point and AEs will grow as large as needed for given source.

## Slide 7: Big Question: How good is the stiff AE transport approximation at high spectral density expected in reactors?
In a reactor, the AE spectrum gets more dense:
Two things might happen:
Mode overlap gets easier  transport gets even stiffer.
Increased mode-mode coupling  transport gets less stiff
decreasing
r*
CGYRO nonlinear AE flux tube
in a reactor
in DIII-D

## Slide 8: Could the massive predicted performance loss in steady state be ameliorated by a dense AE spectrum?
E.M. Bass and C. Holland, IAEA 2023, in prep. for JCP
Could the stiff transport assumption – informed by experiments and simulations performed at experimental mode densities – relax in a reactor due to higher AE mode density?
consider flux tube @ r=0.6
AEs are driven at r=0.6 well above the stiff-transport threshold identified by TGLF-EP  good case study.
C. Holland et al., JPP 89, 905890418 (2023)
YES!

## Slide 9: The AE spectrum is denser in a reactor. Does this change the nonlinear dynamics (spoiler: yes)?
ITG/TEM
AE
AE
Consider the Holland use-case steady-state compact reactor scenario (UCSS) at r=0.6.
C. Holland et al., JCP, 2023; 89(4)
Dn=2
DIII-D: 3-6 AEs
Compact
reactor
: >30 AEs
Use nonlinear CGYRO to explore how mode density affects saturation dynamics.
Dn=8
UCSS
r = 0.6
Consider only AE range of kq, no microturbulence.

## Slide 10: CGYRO (current) and GYRO (old) gyrokinetic codes differ in grid handling, timestepping, and default settings.
CGYRO
GYRO
Both codes: linear or nonlinear gyrokinetic time solvers for tokamaks formulated in high-n ballooning () limit.
Hybrid (IMEX), fixed time step
Explicit spatial radial grid
Global or local (flux tube)
CPU only
Implicit, adaptive time step
Spectral radial grid
Local (flux tube) only, with optional profile shearing
CPU or GPU
Although neither code was formulated with AEs (or any lower n modes) in mind, still holds well for AEs even at experimental values of r*.

## Slide 11: In AE-only CGYRO simulations, increasing mode density makes EP flux decrease…
2 modes
Huge AE amp. & a transport
Would have caused “field blowup” in GYRO.
4 modes
~1/4 a transport
with C=2
(quasi-convective)

## Slide 12: …but EP flux goes up and down again as toroidal resolution increases.
8 modes
16 modes
(half torus)
Tracer microturbulent
transport

## Slide 13: Higher AE mode density in a reactor leads to far less stiff EP transport and maybe a higher onset gradient.
The TGLF-EP+Alpha model assumes much higher transport stiffness than seen in CGYRO with 4+ modes.
(Only finite for numerical reasons)
Predicted diffusivity
Possible route forward: Train a neural net on CGYRO to match the right stiffness (and threshold?) with actual r*.
UCSS

## Slide 14: Main points
Stiff (critical gradient) models of fast-ion driven Alfvén eigenmode (AE) transport work well in many DIII-D discharges
The denser AE spectrum of reactor-like r* allows for nonlinear saturation that is far less stiff  AEs less likely to degrade performance than previously predicted
Even the onset gradient of AE transport (i.e., the critical gradient) could be slightly pushed up by reactor-like AE spectrum density.
Reduced models of transport by energetic particle (EP)-driven AEs – such as TGLF-EP+Alpha – need updates to account for this saturation mechanism to accurately treat reactors.

## Slide 15: Future work
Carefully check radial resolution convergence, especially in half-torus (16 mode) simulation.
Test resolution convergence in radial (possible) and toroidal (less likely) dimensions.
Explore dense-spectrum AE saturation over much more of reactor parameter space.
Develop a simple rule or train a neural net for when and how dense AE-spectrum saturation occurs  incorporate into TGLF-EP+Alpha.

## Slide 16: Background: TGLF-EP+Alpha models DIII-D neutral beam ion-driven AEs well.
Stored energy
Bass et al. APS-DPP 2019
Van Zeeland et al., NF 2024
Collins et al. IAEA 2021
EP pressure
qmin=1 case
qmin=2 case
Super-H case
All are DIII-D shots.

## Slide 17: Projected reactors have r* 3+ times smaller due to larger size and higher Bt , giving a much denser AE spectrum
At mid-core, r=a/2:
for alpha particles in a reactor.
with
higher field
larger size
Perpendicular wave number
in a reactor
in DIII-D

## Slide 18: TGLF-EP+Alpha enters STEP workflow as a TGYRO sub-step (consider simpler case of beam-free fusion)
TGYRO
Iterative thermal-species transport solver
NEO
Neoclassical transport
TGLF
Turbulent transport
CHEF
Heating, current drive and diffusion
CHEASE
Fixed-boundary Grad-Shafranov solver
NEO
Bootstrap current
ONETWO
Classical EP profile
EPED
Pedestal
height + width
Solution
Equilibrium, heating, current
https://omfit.io/modules/mod_STEP.html
Newly-integrated TGLF-EP+Alpha EP transport iterates with TGYRO
Focus of this poster

## Slide 19: The TGLF-EP+Alpha model can enter into any workflow through statefile translators.
TGLF-EP
(critical-gradient
finder)
Alpha
(transport solver)
Profiles and shaping via input.gacode
Critical-gradient file
+ input.gacode
New input.gacode w/ updated:
EP density
Ion and electron power profiles
This has already been done for the Integrated Plasma Solver (IPS) – FASTran workflow.
Any thermal transport solver
input.gacode
yourstate.file